## Slide 1: HEADTAIL simulation studies of Landau damping through octupoles in the LHC.
E.Metral, N.Mounet, B.Salvant, R.Wasef
09/08/2011

## Slide 2: Objective
HEADTAIL
-> average position
-> tune-shift
-> stabilizing current
THEORY
-> tune-shift
-> stabilizing current
-> stability diagram
Compare HEADTAIL and Theory and try to plot the stability
diagram using HEADTAIL
-Im(ΔQ)
Re(ΔQ)

## Slide 3: Main parameters
Single bunch
Energy: 3.5 TeV
Collimator settings: MD May 17th 2010
Impedance: Only dipolar component
Linear bucket
Intensity: 1.15e11 p/b
Horizontal chromaticity: 6

## Slide 4: Average horizontal position & Imaginary tune-shift
Rise-time = 4.02s which leads to Im(ΔQ)= -3.5 E-6
3 different fits with 3.9 ; 4 and 4.1 as time constant
Mode 1

## Slide 5: Real tune-shift
Obtained with an FFT of the average horizontal position
Re(ΔQ)= -9.28 E-5

## Slide 6: Sacherer's analysis
with
with
ΔQ= -1.64 E-4 – i 3.78E-6

## Slide 7: Stability diagrams
-16 A
+26.5A
-37 A
+31A
Gaussian distribution
Parabolic distribution
HEADTAIL: between -5 and -10A
HEADTAIL: between +10 and +15A
HDTL tune-shift
Sacherer tune-shift
Re(ΔQ)
-Im(ΔQ)
Re(ΔQ)
-Im(ΔQ)
Re(ΔQ)
-Im(ΔQ)
Re(ΔQ)
-Im(ΔQ)

## Slide 8: Resonator Impedance
To scan the curve of stability, a broad-band impedance model is used to obtain a second point on the curve
With:
The resonance angular frequency:
Quality factor:
Shunt Impedance:

## Slide 9: Resonator Impedance
Sacherer for LHC_dipolar
HDTL for LHC_dipolar
R=7.1MΩ/m, Q=0.5 f =0.75GHz
R=17.5MΩ/m, Q=1 f =0.64GHz
R=17.5MΩ/m, Q=1 f =0.6GHz
R=17.5MΩ/m, Q=2 f =0.6GHz
R=22.5MΩ/m, Q=1 f =0.1GHz
Re(ΔQ)
-Im(ΔQ)

## Slide 10: Comparaison Sacherer/HDTL/MOSES
 | Rs (Mohm/m) | 7.1 | 17.5 | 17.5 | 17.5 | 22.5 | 7 | 9.86
 | Q | 0.5 | 1 | 1 | 2 | 1 | 0.5 | 0.5
 | f(GHz) | 0.75 | 0.64 | 0.6 | 0.6 | 0.1 | 0.75 | 1.5
Headtail | Re | 1.42E-05 | 5.28E-05 | 4.49E-05 | 4.11E-05 | 7.63E-06 | 1.11E-05 | -5.24E-05
 | Im | -1.12E-05 | -3.16E-05 | -3.06E-05 | -1.93E-05 | -2.95E-06 | -1.14E-05 | -0.000011619
MOSES | Re | 1.05E-05 | 3.23E-05 | 3.17E-05 | 2.25E-05 | 3.80E-06 | 1.03E-05 | -6.48E-05
 | Im | -1.14E-05 | -3.13E-05 | -3.10E-05 | -1.97E-05 | -3.89E-06 | -1.12E-05 | -7.82E-06
 | error RE | 26 | 39 | 29 | 45 | 50 | 7 | 24
 | error Im | 2 | 1 | 1 | 2 | 32 | 2 | 33
Sacherer | Re | 4.85E-06 | 3.09E-05 | 3.27E-05 | 2.57E-05 | 4.74E-06 | 4.78E-06 | -8.36E-05
 | Im | -1.72E-05 | -3.43E-05 | -3.39E-05 | -2.32E-05 | -3.67E-06 | -1.70E-05 | -5.29E-06
 | error Re | 66 | 41 | 27 | 38 | 38 | 57 | 60
 | error Im | 55 | 8 | 11 | 20 | 24 | 49 | 54

## Slide 11: Scan at -30A
R=24.5MΩ/m, Q=0.55 f =1.55GHz
R=18.9MΩ/m, Q=0.55 f =1.3GHz
R=27.67MΩ/m, Q=1 f =1GHz
R=25.415MΩ/m, Q=2 f =0.9GHz
R=12.89MΩ/m, Q=1.5 f =0.6GHz
Re(ΔQ)
-Im(ΔQ)

## Slide 12: Head-Tail and not TMC

## Slide 13: Head-Tail and not TMC