## Slide 1
General
  mode matching for transverse impedance being compared with CST and infinitely long pipes (Nicolo)
  Carlo found a way to disentangle direct space charge from CST simulations with low beta.
  Work of Berengere to benchmark resonance parameters obtained from eigenmode and wakefield simulations (transverse and longitudinal).
HL-LHC
  Deadline: Beam induced heating for end of Summer
  Deadline: impedance model for November
Impedance working group update 07th August 2013

## Slide 2
LHC
  Wire measurements on new RF fingers design completed by Olav and Joseph.
  Wire measurements on TCTP prototype with Andrea, Joseph, Carlo and Patrice: it will be very hard to identify the potentially harmful transverse mode. This was also confirmed by simulations with wires. Will improve the setup and try 2 wire measurements.
  Mikhail Zobov and Oscar Frasciello (INFN) (re-)computed the geometric impedance of the current LHC collimators with very fine meshes with GdfidL, for simulated bunch length of 5mm and 7.5cm, enabling to find the low frequency impedance value that seems close to what Alexei obtained in the past. Transverse kick factors were also computed and compared to the resistive-wall one (both analytic formula for classic thick wall and by Nicolas using the definition + his flat chamber theory), showing that for tungsten the geometric kick factor is always larger than the resistive-wall one, while for CFC it becomes larger for half-gaps bigger than 7mm. In any case the geometric impedance of collimator seems to be rather important and underestimated in the current LHC impedance model, which goes in the right direction to explain last years’ observations on tune shifts. Work is ongoing to get the full geometric impedance / wake function of collimators.
  LTEX review for ALFA and TOTEM: no showstopper identified for the consolidation and upgrade before the measurements start (wire measurements started this week by Olav for ALFA).
  Non-conformities in RF contacts: talk foreseen at LBOC to gather related info by the end of August (deadline). Nothing seen on vac or cryo observables.
  BGV: several meetings with BI and LHCb. The reduction in the foreseen diameter from 147 mm to 106 mm solved a lot of issues and enables to stay within a more reasonable impedance range (berengere).
  MKI: MKI8D which had a very different behaviour from the others was found to have a serious manufacturing issue (90 degrees twist of the contacts from one end to the other).
  ECR for the spare experimental chamber of ATLAS in case the smaller diameter option does not work for some reason. Small impact foreseen.
  Titanium/Carbon pipe ready for bench measurements.
  TDI: a coating of 1 micron is under preparation (EN/STI and TE/VSC).

## Slide 3
SPS
  High bandwidth feedback review on July 31st: impedance of the planned options (stripline and slotline) were computed and are expected to be small compared to the rest of the machine. Paragraph will be written by Carlo for the design report (deadline).
  Wirescanner: practical solution not found yet. Will study the coupler option before the MSWG talk foreseen for August 27.
  Studies continue to hunt the longitudinal resonant modes beyond 1 GHz (ZS pumping ports, BPMs, flanges, etc).
  ECR to replace TPSN with TPST in LSS2: question about impedance shielding to be solved with Bruno Balhan.
PS
  Very nice effort of the “Sapienza gang” to produce the PS impedance model in time for the TDR of LIU-PS. As for LHC and SPS, we miss a significant percentage compared to tune shift measurements.
  Deadline: TDR chapter written by Mauro to be completed and given to Simone by mid-August.
PSB
  Impedance model: Carlo simulated the indirect space charge of the ring and geometric impedance of transitions using the layout provided by Olav. Work on-going to understand the tune shift measurements of Diego at different energies.
ELENA:
  Studie for resistive wall and stripline on-going.
TLEP:
  Nicolas is “convener” for collective effects (together with Ralph Assmann and Simon White).