## Slide 1: Electromagnetic Simulations of VMTSA Equipped with the Longer RF Fingers
O. Kononenko
BE/RF
LRFF Meeting, CERN, August 21, 2012

## Slide 2: Introduction
Study of the long RF fingers and comparison with the measurements
Many ways to deform the fingers, the gap has been introduced in CST modeller in the simplest way
Different gap sizes have been studied

## Slide 3: RF Fingers Deformation in VMTSA

## Slide 4: Simulated Models
Conforming
fingers
Wire,
conforming
fingers
Bad contact 1st type
Wire,
no fingers
Bad contact 2nd type
Ferrites in, Philips 8C11
Wire,
20-40mm gaps
Completed
In progress
Old longer fingers
New shorter fingers
Conforming
and bad contact
fingers

## Slide 5: VMTSA with Wire and No Fingers
Port 1
Port 2
Copper
Perfect H
Model:
  180 deg of the structure
  copper outer walls
Simulation profile:
- second order basis functions
  curvilinear elements enabled
  0.01 s-parameters accuracy => ~170K tet10 mesh
  discrete sweep from 20MHz to 2GHz, 10MHz step
Wire

## Slide 6: Transmission, no Fingers
Jean-Luc Nougaret, VMTSA measurements,
December 2011-January 2012
Good agreement of the CST/HFSS/Measurements results

## Slide 7: VMTSA with Wire and Comforming Fingers
Port 1
Port 2
Copper
Perfect H
Model:
  180 deg of the structure
  copper outer walls
Simulation profile:
- second order basis functions
  curvilinear elements enabled
  discrete sweep from 20MHz to 2GHz, 20MHz step
  0.01 s-parameters accuracy => ~220K tet10 mesh
Wire
- no matching

## Slide 8: VMTSA with Wire and Deformed Fingers: 20-40mm gaps
Port 1
Port 2
Copper
Perfect H
Model:
  180 deg of the structure
  copper outer walls
Simulation profile:
- second order basis functions
  curvilinear elements enabled
  discrete sweep from 20MHz to 2GHz, 20MHz step
  0.01 s-parameters accuracy => ~260K tet10 mesh
Wire
Gap: 20-40mm
Gap
- no matching

## Slide 9: Transmition for Different Gap Sizes
Transmission level is quite different, may be because there was a matching load in the measurements?
30mm gap simulations give the best agreement for the resonances. Gap shape could be different in the simulation/measurement so it is quite complicated to have full agreement.

## Slide 10: Reflection for Different Gap Sizes

## Slide 11: CST TD Simulations of VMTSA
Model:
  full structure
  copper walls
  conforming fingers and 30mm gap
Simulation profile:
- 10 lines per wavelength
- refine at PEC by factor 6
- 70mm bunch sigma
  400K hex mesh

## Slide 12: Longitudinal Wake Potential
No surprise: introducing a gap we’re getting unwanted modes with high Q

## Slide 13: Longitudinal Impedance Re(Z)
Some of the resonances could also be seen in the wire simulations

## Slide 14: Tangential Component of Magnetic Field for Conforming Fingers

## Slide 15: Tangential Component of Magnetic Field for 30mm gap
Unwanted modes with high Q have been excited near to the deformed fingers

## Slide 16: HFSS Eigen Mode Analysis of 30mm Gap
Most of the modes have been excited by 30mm gap, just some of them are eigen modes of the bellows.
Loss Density for the First Eigen Mode at 290MHz
Loss denstity distribution looks similiar to CST.
These frequencies and losses crucially depend on the gap size and shape.

## Slide 17: Conclusions
Long fingers with good contact => no impedance problems, no surprise
Bad contact => impedance problems depending on the gap size/shape
Need to measure ferrites properties to accomplish ferrites simulations