## Slide 1: BSRT: numerical evaluation of RF induced heating

## Slide 2
Axis of symmetry
Ferrite
Cu coating
ANALYSIS
General Constraints:
2D axisymmetric analysis
Ferrite ring – Re=30; Ri=16; h=6 [mm]
Power on ferrite: 10÷50 W
 | emissivity [-]
steels (304L) | 0.3
Cu coating | 0.05
Ferrite | 0.8
Not axisym. in reality
No mirror
first approximation with all steels304L

## Slide 3
CASE 1:
best case scenario for evacuation only through radiation
Consistent with analytical estimations
Tferrite_MAX=390°C
P=50W
Ferrite radiates to ambient (blackbody of emiss.=1) other components are neglected
TAMBIENT=22°C
T [°C]

## Slide 4
CASE 2:
T [°C]
P=50W
Ferrite radiates to other components
No Contact: all inner components exchange heat only through rad. (also with external vacuum tank)
Vacuum tank cooled by external free convection (α=5W/m2K, TAMBIENT=22°C)
Tferrite_MAX=560°C

## Slide 5
CASE 3a:
Is cooling of external tank interesting in case of evacuation of ferrite heat only through radiation?
T [°C]
Tferrite_MAX=557°C
P=50W
Ferrite radiates to other components
No Contact: all inner components exchange heat only through rad. (also with external vacuum tank)
Vacuum tank at constant TTANK=22°C

## Slide 6
CASE 3b:
P=50W
Ferrite radiates to other components
Contact between mirror support and flange : all other inner components exchange heat only through rad. (also with external vacuum tank)
Vacuum tank at constant TTANK=22°C
Tferrite_MAX=553°C
Ferrite temperature is very slightly affected by cooling methods and T of vacuum tank
T [°C]

## Slide 7
CASE 4:
P=50W
Ferrite radiates to other components
all other inner components exchange heat through rad. (also with external vacuum tank)
CONDUCTION: Thermal contact chain from ferrite to flange
Vacuum tank cooled by external free convection (α=5W/m2K, TAMBIENT=22°C)
INTERFACE | Th.Conductance [W/m2K]
Ferrite-AxialRF | 40
AxialRF-RadialRF | 500
RadialRF-Support | 500
Support-Flange | 1600
pressed by approx. 100kg
Tferrite_MAX=460°C
Temperature drop of 100°C w.r.t case 2
How tank is cooled becomes interesting

## Slide 8
CASE 5:
P=10W
Ferrite radiates to other components
No Contact: all inner components exchange heat only through rad. (also with external vacuum tank)
Vacuum tank cooled by external free convection (α=5W/m2K, TAMBIENT=22°C)
T [°C]
Tferrite_MAX=286°C

## Slide 9
Preliminary Conclusions:
For P=50W, if heat is evacuated only through radiation it is impossible to keep ferrite temperature below Tcurie of the grade (case 2-3)
Cooling also by conduction is highly beneficial (case 4)
Changing ferrite to a grade with higher Tcurie is effective only if RF induced power is 10W condition (case 5)