## Slide 1
Overview of LHC Collimators
RF system
LHC RF Fingers Task Force 30.10.2012 A. Bertarelli F. Carra, A. Dallocchio, M. Garlaschè, L. Gentini, N. Mariani, R. Perret, …
With invaluable input by S. Calatroni

## Slide 2: Outlook
    Specifications
    Phase I
    TCLIA & TCTVB
    Phase II
    TCLD
    TCTP
    Conclusions

## Slide 3: Context
    Focus on RF design of main variants of LHC Collimators:
      Phase I: TCP, TCSG, TCTA, TCLP, TCLIA, TCTVB …
      Phase I Upgrade: TCTP, TCSP …
      DS Collimators: TCLD
      Phase II: TCSM

## Slide 4: RF Impedance Specifications
    First specification on RF impedance budget for Phase I by F. Ruggiero (25.06.2003)  Collimator Impedance Budget (Transverse) 330 MW/m
    Additional requirement (F. Ruggiero –June 2004)  Integral Contact Resistance (on each transition) ≤ 1 mW

## Slide 5: Phase I Design Baseline
    RF Specifications led (along with other inputs) to following design decisions:
      Carbon-based jaws with lowest possible electrical resistivity for (Phase I) Primary and Secondary Collimators 
        Jaw Material: Across Corp. (Tatsuno) AC150K Carbon/Carbon (r  7 mWm)
        No thin metallic coating (e.g. Cu) on jaw surface
      Separate (0.15 mm gap) Tungsten (Inermet 180) blocs for Tertiary Collimators.
      RF Contacts:
        Longitudinal Contacts (Jaw-Vacuum Chamber): Ag-coated CuBe (C17410 TH02)
        Transversal Contacts (Jaw1-Vacuum Tank-Jaw2): Ag-coated CuBe (C17200 TH02 off-the-shelf strips by Feuerherdt)
        Transition Contacts (Vacuum Chamber-Vacuum Tank):

## Slide 6
Uncoated CuBe fingers sliding on C/C
Electrical Contact Resistance ~ 30 mW (specification: 1 mW)  Redesign necessary.
  Longitudinal Contacts: Initial Proposal for 1st (SPS) Prototype (2003)
Phase I Design Baseline

## Slide 7: Phase I Design Baseline
Jaw assembly
Longitudinal RF fingers (15x3 mm CuBe 17410 5mm Ag coating)
Outer ring (304L)
Ni (1 mm) +Rh (2 mm)
RF-finger Stroke
Restraint (304L)
  Longitudinal Contacts: Final Design (All Phase I variants)
Inner ring (304L)
Ni (1 mm) +Rh (2 mm)
Transition RF fingers (11x3 mm CuBe 17410 5mm Ag coating)
RF finger assembly screwed to jaw

## Slide 8: Phase I Design Baseline
Longitudinal Fingers. Lessons learnt:
  Adopt appropriate steps to avoid stick-slipping (tolerance chain, geometry, coatings, de-burr …)
  Use stroke restraint to limit RF finger azimuthal movements.

## Slide 9: Phase I Design Baseline
RF Transverse Strips (CuBe 17200 5mm Ag coating)
  Longitudinal Contacts: Final Design (TCP, TCSG, TCTA, TCTP …)

## Slide 10: Phase I Design Baseline
Four clamps, each one equipped with two contact strips (0.15 mm CuBe 17100 5mm Ag-coating) of different length (type 1 – 276 mm and type 2 – 316 mm)
1.5 mm Logitudinal rail (electropolished 304L)
Spring system to keep fingers in contact with rail at moderate force (~18gr/finger)
RF contacts must withstand a wear equivalent to ~20000 cycles (open-close of the jaw) → ~1.4 km !
RF contact strip type 2
RF contact strip type 1
Clamp
Jaw
  Tranverse Contacts: Final Design (TCP, TCSG, TCTA, TCTP …)

## Slide 11: TCLIA/TCTVB Design
As opposed to PhaseI “1 beam per tank” collimators, “2 in 1” designs (TCLIA and TCTVB), ferrite was added to standard sliding contacts to damp HOM in large cavities (A. Grudiev simulations).
Ferrite was also added in transitions.
Ferroxcube 4S60 Ferrite
Longitudinal Ferrite Tiles (2x13) 30x100x6mm3
Transition Ferrite Tiles (2x2x) 60x60x6 mm3
OF-Cu Shield (1.5 mm)
316LN Shield (1.5 mm) 0.2mm Cu-coated
RF Transverse Strips (CuBe 17200 5mm Ag coating)

## Slide 12: TCLIA/TCTVB Design

## Slide 13: TCLIA/TCTVB Design
RF Fingers in contact
RF fingers not in contact
RF issue? Visual inspection of TCTVB.4L2 on 03.02.2012 (O. Aberle EN/STI)

## Slide 14: Phase II Design Baseline
Phase II RF design was triggered by the requirement to avoid sliding contacts between RF strips and St. Steel Rail  In 2008 it was decided to replace RF contacts with Ferrite Tiles
Doigt #10

## Slide 15: Phase II Design Baseline
3 Jaw sectors independently supported on rigid back stiffener for enhaced geometrical stability.
Modular design allowing flexibility in the active jaw material choice
Fine-adjustment system
Mo Back-stiffener
Jaw Sectors
RF shield
RF contacts (sector-sector and sector-support)

## Slide 16: Phase II Design Baseline
Ferrite tiles

## Slide 17: Phase II Impedance Studies
H. Day (BE/ABP)

## Slide 18: Phase II Impedance Studies

## Slide 19: DS (Warm) Collimator (TCLD)
RF extremity fingers
Horizontal fixed contact
Vertical mobile contact
RF Bridge
RF screen contacts
RF screen/tank contact
BEAM

## Slide 20: DS (Warm) Collimator (TCLD)
Ferrites

## Slide 21: TCLD Impedance Studies

## Slide 22: TCTP Design Baseline
Same extremity RF contacts of phase I collimators
Ferrite tiles replacing longitudinal RF strips

## Slide 23: TCTP Design Baseline
Change of jaw tapering to accommodate BPM buttons
C17200 spring-like contacts added between Glidcop and each W extremity bloc (0.6 mm pre-compression)
Phase I
TCTP

## Slide 24: TCTP RF System: materials
Ferrite proposed for TCTP collimators: TT2-111R Trans-Tech
Higher Curie Temperature: 375 ˚C
What is the best solution for the support material?
Ferrite
Supports

## Slide 25: TCTP RF System: materials
Case 1: nominal LHC operation
Case 2: High-Luminosity LHC
Case 3: High-Luminosity LHC, with reduced bunch length (0.5 ns)  Pessimistic case
Heat losses (uniformly distributed along the longitudinal coordinate) |  | 
 | Total power on collimator [W] | Power loss on 1 ferrite array [W]
Case 1 | 20 | 1
Case 2 | 110 | 6
Case 3 | 375 | 20
RF losses on ferrite evaluated by BE/ABP (H. Day, B. Salvant)
Safety factor of 2 considered for the loads reported in the table below

## Slide 26
Pure copper OFE: worst choice, penalized by copper low emissivity
Stainless steel: temperature up to 150 ˚C in the worst case scenario, with a safety ratio > 2 with respect to the Curie Temperature
Copper OFE with CrO coating: best choice from the thermal point of view, temperature on ferrite decreased by 25-30% with respect to stainless steel (this reduction could be ~ 40% when the upper screen is also coated with CrO)
TCTP RF System: materials

## Slide 27
Black Chrome
Graphite
Black chrome presents a dusty surface (risk of particles detachment)
SEM observations performed by N. Jimenez Mena compared morphology and porosity of Black Chrome and Graphite (EDMS n. 1220547)
“The Cr coating shows many cracks and some inhomogeneity on the surface. However, the porosity and discontinuities in the graphite reference seem to be higher.”
TCTP RF System: materials

## Slide 28
The best thermal treatment on TT2-111R ferrite still has to be defined
First measurements by G. Cattenoz on samples treated 24h in air and 24h in vacuum at 400 ˚C showed high ferrite outgassing rates
A second thermal treatment has been launched (48h in air and 48h in vacuum, T = 1000 ˚C): results expected in the next weeks
Chart: 1/T [1/K]
| 3.3766999999999998E-3 | 3.3766999999999998E-3 | 3.3766999999999998E-3 | 3.3766999999999998E-3 | 3.3766999999999998E-3 | 3.1730999999999999E-3 | 3.0198E-3 | 3.0016999999999999E-3 | 2.8722999999999999E-3 | 2.8641000000000001E-3 | 2.7766000000000002E-3 | 2.7766000000000002E-3 | 2.6584999999999998E-3 | 2.6584999999999998E-3 | 2.5763000000000001E-3 | 2.5763000000000001E-3 | 2.4865999999999998E-3 | 2.4805000000000001E-3 | 2.3915E-3 | 2.3915E-3 | 2.3086999999999999E-3 | 2.3086999999999999E-3 | 2.2314000000000001E-3 | 2.2314000000000001E-3 | 2.1591000000000002E-3 | 2.1591000000000002E-3 | 2.1591000000000002E-3 | 1.9678999999999999E-3 | 1.9678999999999999E-3
H2 Outgassing from unfired SS - Baked at 300C | 4.29e-12 | 4.08e-12 | 3.74e-12 | 3.87e-12 | 4.29e-12 | 1.45e-11 | 3.68e-11 | 3.88e-11 | 7.71e-11 | 7.88e-11 | 1.33e-10 | 1.39e-10 | 2.5e-10 | 2.61e-10 | 3.64e-10 | 3.68e-10 | 6.27e-10 | 6.53e-10 | 1.08e-09 | 1.26e-09 | 2.54e-09 | 2.18e-09 | 4.14e-09 | 3.76e-09 | 5.28e-09 | 4.18e-09 | 5.41e-09 | 9.95e-09 | 1.05e-08
H2 Outgassing from Fired SS - Baked at 300C | 1.4819e-14 | 1.8935e-14 | 1.5995e-14 | 2.4227e-14 | 1.8464e-14 | 2.8814e-14 | 4.7278e-14 | 7.0682e-14 | 1.2114e-13 | 4.7161e-13 | 4.4456e-12 | 4.0575e-12
Ferrite CMD5005 vac compatible as received | 6.1991e-12 | 6.2947e-11 | 1.5789e-10 | 2.8601e-10 | 4.8179e-10 | 8.0742e-10
Ferrite disk MKI as received | 1.5853e-12 | 2.4912e-12 | 1.2682e-11 | 5.5485e-11 | 2.4346e-10 | 3.4763e-09
Ferrite TT2-111R after TT 400C air and TT 400C vac | 5e-11 | 1.4705e-10 | 1.2471e-10 | 5.137e-10 | 3.1309e-10 | 7.9863e-10 | 8.6243e-10 | 3.5834e-09 | 1.1556e-08 | 1.1412e-08
TCTP RF System: materials

## Slide 29
  Backup slides

## Slide 30
Phase I Design Baseline
C17200: high mechanical properties (σ0.2 = 1240 MPa)
C17410: high conductivity, residual elasticity after heat treatment
Silver coating to increase surface contact conductance
C17200 Stress relaxation at σ = 0.75σ0.2
C17410 Stress relaxation at σ = 0.75σ0.2

## Slide 32
Phase I Design Baseline

## Slide 33
f= 0.996 GHz
Q = 2550
Ploss = 170 W
Prf-finger = 1.1W
For nominal LHC intensity
Calculations by A. Grudiev showed high power losses on the longitudinal RF fingers
TCLIA/TCTVB Impedance

## Slide 34
Q = 26
Ploss ~ 0.5 W
Addition of ferrite reduces RF losses by a factor 3
TCLIA/TCTVB Impedance

## Slide 35
(a) Horizontal driving and (b) vertical driving impedance of all materials
SiC: significantly higher impedance than graphite collimators
Metallic design: lower in all frequencies for imaginary transverse, lower/comparable in real transverse
Phase II Impedance

## Slide 36
Longitudinal impedance of the DS collimator. Revision 1 indicates a collimator with RF clips, revision 2 is with slightly modified RF finger structure in the transition piece. For comparison the design longitudinal impedance Z/n = 0.1 Ω.
TCLD Impedance Studies

## Slide 37
Calculation by B. Salvant → With ferrite, frequency decreases and all transverse modes are damped. However, low frequency (<100 MHz ) impedance increases (factor 2).
Ferrites helps significantly also in the longitudinal plane
TCTP Impedance Studies