## Slide 1: Dealing with ferrite heating: Figures OF Merit And design guidelines
LRFF Meeting - 20.11.2012
A. Bertarelli, M. Garlaschè (EN-MME)

## Slide 2
Analysis introduction
The goal:
Determine figures of merit for maximum RF induced power on ferrite before TCURIE is reached
The assumptions:
Steady-state regime and uniform ferrite temperature distribution (regardless of actual RF power deposition)
Ferrite tile is of arbitrary cross section
Ferrite radiates from all sides with equal emissivity (0.8)
Completely surrounding heat sink & no intermediate components between ferrite & sink (ferrite view factor equal to 1)
2D simplification of ferrite tile, i.e infinitely long geometry (no end effects)
Heat sink with uniform emissivity and temperature

## Slide 3
Analysis introduction
The equation:
Q : [W/m2] radiated heat per ferrite surface unit
σB : Stefan-Boltzmann constant
T0 : temperature of surrounding heat sink
KG : geometry and RF power deposition coefficient (KG≡1 thanks to hyp. # I)
Kε : radiation exchange coefficient, function of emissivity and geometry

## Slide 4
Analysis output
KA
If KA is high no need for very high ε0
CASE:
εFERRITE =0.8
TCURIE = 150°C
T0=22°C (i.e. cooled heat sink)
Specific power w.r.t. ε0 & KA
But ferrite needs to be held, i.e. KA is usually near to one.
E.g. TCTP collimator:
KA~=1.6
KA=1
KA=1.6
KA=10
KA=50
KA=100
Q [W/m2]
ε0 [-]
Notes: KA_MKI=2.9

## Slide 5
Analysis output
Heat evacuation can be handled by radiation only (regardless of geometry)
Need for ferrite active cooling
Output is geometry dependent
Legenda:
CASE:
εFERRITE =0.8
TCURIE = 150°C
T0=22°C (i.e. cooled heat sink)
Critical design zone
High KA point of interest
Q [W/m2]
ε0 [-]
Low KA point of interest

## Slide 6
Analysis output
Points of interest obtained for different values of TCURIE
Heat evacuation can be handled by radiation only (regardless of geometry)
Need for ferrite active cooling
Output is geometry dependent
Legenda:
27
150
275
400
530
Q [W/m2]
TCURIE [°C]
0
5e3
1e4
1.5e4
2e4

## Slide 7: BACK UP

## Slide 8
Analysis output
Power plots obtained for different values of TCURIE
Tcurie [°C] |  | 
100 | 127 | 519
150 | 264 | 1076
200 | 459 | 1869
250 | 727 | 2959
375 | 1824 | 7423
500 | 3777 | 15372
27
150
275
400
530
TCURIE [°C]
0
5e3
1e4
1.5e4
2e4
Q [W/m2]

## Slide 9
Analysis output
KA=1
KA=1.6
KA=10
KA=50
KA=100
CASE:
εFERRITE =0.8
TCURIE = 250°C
T0=22°C (i.e. cooled heat sink)
Specific power w.r.t. ε0 & KA
Q [W/m2]
ε0 [-]

## Slide 10
Analysis output
KA=1
KA=1.6
KA=10
KA=50
KA=100
CASE:
εFERRITE =0.8
TCURIE = 375°C
T0=22°C (i.e. cooled heat sink)
Specific power w.r.t. ε0 & KA
Q [W/m2]
ε0 [-]