## Slide 1: SPS Transverse Damper System

## Slide 2: Overview
What is it used for ?
How does it work ?
Control and Diagnostics
Electronic details

## Slide 3: What is it used for ?
Damping of transverse injection errors
Feedback: to cure transverse coupled bunch instabilities
Excitation of transverse oscillations for beam measurements (Multi-Q) and increase of emittance (blow up)

## Slide 4: How does it work ?
A feedback loop including :
  Pick-ups (2.04 => 2.15)
Associated by pairs according to the beam type
  A Low Level part
(Signal process + Pick-up Mixing + Low Level)
  4 “electrostatic” kickers (H1, H2, V1 and V2)
H1, H2 and V1 Installed in LSS2-
V2 installed in LSS2+

## Slide 5: Feedback Loop
BEAM
Position
monitor
Beam
deflector
Low Level
Surface – BA2
+
-

## Slide 6: Association of the Pick-ups
2.04 2.06 | H plane LHC | 2.08 2.10 | H plane - Ions (before) | 2.12 2.14 | H plane Fix Target
2.05 2.07 | V plane LHC | 2.09 2.11 | V plane - Ions (before) | 2.13 2.15 | V plane Fix Target
Used as spares

## Slide 7: The Pick-ups (position monitors)
BDH 2.04 BDV 2.05
 Shared with BI (MOPOS) but specific electronics

## Slide 8: Block Diagram (H1 & H2)

## Slide 9: Simplified Block Diagram (H1 & H2)
2 pick-ups
2.12
&
2.14
Fixed Target beam
2 pick-ups
2.04
&
2.06
LHC beam
D
D
S
S
Level adjust.
Pick-ups Mixing
Betatron phase adjust.
Closed orbit suppr.
Delay adjust.
Timing ON/OFF
External excitation
Gain LSA
Gain LSA
Timing ON/OFF
External excitation
Damper H1
BDH 214.37
( )
Closed orbit suppr.
Delay adjust.
Damper H2
BDH 214.51
( )
Level adjust.
Level adjust.
Level adjust.

## Slide 10: The electrostatic kickers
BDH 214.37 (H1)
BDH 214.51 (H2)
BDV 214.57 (V1)
BDV 221.76 (V2)
 LSS 2 -
 LSS 2 +

## Slide 11: Control and Diagnostics
Control  New RF Control Application (MMI)
 Trim Editor Application (LSA)
Diagnostics  Oasis Application
            Compare with reference signals

## Slide 12: New RF Control Application
More ergonomic
All parameters readable
Role based access to change settings
Synoptic :
Experts view / Simplified view for Operation

## Slide 13: Block Diagram (H1 & H2)
2.12 & 2.14
2.04 & 2.06
timing
timing
Multi-Q
LSA
LSA
New
MMI
New
MMI

## Slide 14: Dampers H1 & H2 (simplified)
2 pick-ups
2.12
&
2.14
Fixed Target beam
2 pick-ups
2.04
&
2.06
LHC beam
D
D
S
S
Level adjust
‘DGCA’
Pick-ups Mixing
‘DPUM’
- p.u. select
- Polarity
Phase
Betatron phase adjust.
Closed orbit suppr.
(Notch Filter)
Delay adjust.
Timing ON/OFF
External excitation
Gain LSA
Gain LSA
Timing ON/OFF
External excitation
Damper H1
BDH 214.37
( )
Closed orbit suppr.
(Notch Filter)
Delay adjust.
Damper H2
BDH 214.51
( )
- Controlled by the new MMI application
- Controlled by LSA (Trim Editor Application)
Level adjust
‘DGCA’
Level adjust
‘DGCA’
Level adjust
‘DGCA’

## Slide 15: Diagnostics
Observation with OASIS Application:
    Delta : difference between the signals of one pick-up
      (= not normalised transverse position of the beam
       position * Intensity)
    Sum : sum of the signals of one pick-up
      (= intensity of the beam)
    Input : signal leaving the low level
    Plates : voltage of the kicker’s plates
      (= delta signal between the two plates)

## Slide 16: Diagnostics
Sum
Delta
Input
Plates

## Slide 17: Diagnostics
  Delta signals + BCT (100ms/div)
2.13V and 2.15V (CNGS beam – Damper V)

## Slide 18: Diagnostics
  Sum signals (100ms/div)
2.13V and 2.15V (CNGS beam – Damper V)

## Slide 19: Diagnostics
  Input V2 and Plates V2 signals (100ms/div)

## Slide 20: Diagnostics
Observation | Diagnostic
- Damper Trip | - Reset and restart
- No signals from the Pick-ups (Δ and Σ) | - Bad contact in the tunnel - Problem pre-ampli alimentation
- Phase error on an ‘Input‘ signal | - MMI datas corrupted (software error)
- Amplitude difference between 2 ‘Plates’ signals of the same plane | - Power Problem
Damping too long - Bad damping | - Need more gain (Trim Editor) Wolfgang’s settings Bad Tune

## Slide 21: Few more details..
How the signals are treated in the electronic part of the system ?

## Slide 22: 2.04 D and 2.06 D – H plane (LHC Beam - Single Bunch, scope in SR4)

## Slide 23: Pick-up Mixing
 Betatron phase advance between p.u. and the kicker has to be = 90°
Main * cos F
Aux * sin F

## Slide 24: Pick-up Mixing
Main pu D
Aux. pu D
Vector sum = Main*cos F + Aux*sin F
 Betatron phase adjustment is done by combining 2 “orthogonal” (~ 88°) signals with good signs and good ratios
Vector sum
F

## Slide 25: After Pick-up Mixing

## Slide 26: Low Level
Notch Filter does the difference between 2 turns  delete the closed orbit
Delay is to ensure that the signal arrives at the kicker at the right time (right bunch)
(Delay = Dt + temps de vol du signal)
LSA Gain to be adjusted with the Energy of the Beam (damping time & losses)

## Slide 27: After closed orbit suppression

## Slide 28: Before & after Notch

## Slide 29: Feedback Loop
BEAM
Position
monitor
Beam
deflector
Low Level
Surface – BA2
1st turn: Measurements only
2nd turn: Meas + correct but with orbit offset
3rd turn: Correction OK