## Slide 1: Electron-Cloud Activities for LHC
Frank Zimmermann
ICE Meeting, 24.11.2010

## Slide 2: electron-cloud effects
vacuum pressure rise
  - desorption yield, pumping speed,…
single-bunch instability
  - interplay w. impedance & beam-beam
multibunch instability
incoherent emittance growth
heat load in cold arcs (quench)
perturbation of beam diagnostics

## Slide 3: modeling tools at CERN
ECLOUD (F. Zimmermann, G. Rumolo, et al ++)
- e-cloud build up, electron flux on wall,
heat load, multi-bunch wake field
HEADTAIL (G. Rumolo, F.Z., E. Benedetto,…)
  - e-cloud driven single-bunch instability,
  incoherent emittance growth, interplay
  w. impedance & space charge
  Micromaps (G. Franchetti, E.B., F.Z.)
    - precise incoherent effects
    Faktor2 (W. Bruns, G. Rumolo) for 3D

## Slide 4
schematic of e- cloud build up in LHC arc beam pipe,
due to photoemission and secondary emission
[F. Ruggiero]

## Slide 5
R. Cimino, I. Collins, 2003; CERN-AB-2004-012
probability of elastic electron reflection seems to approach 1 for
zero incident energy and is independent of d*max
yield
dmax
emax
R

## Slide 6
[M. Furman, 1997]
Present Model of Secondary Emission Yield
secondary electrons consist of true secondaries and elastically reflected;
since 2003 we assume that elastic reflection is independent of Q (no data)
[Kirby, 2001;
Henrist, 2002;
Furman, 1997]
true secondaries:
elastic reflection:
[Cimino, Collins, et al., 2003]
this quantum-mechanical formula fits the data well for E0~150 eV
M. Furman includes rediffused electrons and finds that they increase the
heat load by 100%
this d*max
is rescaled
considering
R

## Slide 7: SEY model examples

## Slide 8
N. Hilleret, SPS Scrubbing Day, CERN, 2002
in-situ conditioning in the SPS (2002)

## Slide 9
SPS benchmarking 2004, strip detector simulation
surface conditions (dmax, R) and detector properties are uncertain
constrain parameters by benchmarking multiple measurements
change distance between trains & use relative measurements
two different
bunch train
spacings
two different
pressures
(40 ntorr
and 4 ntorr)
Daniel Schulte

## Slide 10
three curves intersect at dmax=1.35, R=0.3;
flux at later times (F=0.3 mA) dmax=1.2 reached in SPS!
flux: (1) ratio 1&2 trains, (2) two spacings, (3) absolute
Daniel
Schulte
note:
results
sensitive
to pressure,
chamber
geometry,
etc.,
variation:
dmax~1.4-1.3
R~0.1-0.7

## Slide 11
H. Maury Cuna
Simulated heat-load for nominal LHC
need SEY<1.5

## Slide 12
1404 bunches at 7 TeV
H. Maury Cuna
Simulated heat-load for LHC w 50-ns spacing
50 ns should have no problem !?!

## Slide 13: e- cloud can lead to bunch instability

## Slide 14: LHC emittance growth for different re
single-bunch
instability
threshold
~3x1011 m-3
E. Benedetto, Ph.D. Thesis, Politecnico di Torino, 2006
LHC injection, Q’=2,
Nb=1.15x1011
K. Ohmi, F.Z.,
PRL85, 2000

## Slide 15
LHC emittance growth for different Nb
E. Benedetto, Ph.D. Thesis, Politecnico di Torino, 2006
LHC injection,
Q’=2,
re=6x1011 m-3
at re=6x1011m-3
single-bunch
instability
threshold
Nb~6x1010

## Slide 16
LHC emittance growth for different Q’
LHC injection,
Nb=1.15x1011,
re=6x1011 m-3
at re=6x1011m-3
instability
suppressed
for Q’>15
similar to LHC
E. Benedetto, Ph.D. Thesis, Politecnico di Torino, 2006
slow
emittance
growth
below
threshold
slow emittance growth never vanishes; precise value depends on optics & e-cloud distribution around the ring (E. Benedetto, G. Franchetti, F.Z., PRL97:034801,2006)

## Slide 17: surface conditioning

## Slide 18
N. Hilleret, Twostream Instabilities workshop, KEK, 2001
surface conditioning by e- bombardment
1 mC/mm2

## Slide 19
surface conditioning by synchrotron light
N. Hilleret et al, EPAC2000
need 1020 ph/m! with 0.01 ph/m/proton/turn
7 hours with 400 nominal bunches at 3.5 TeV might do??!

## Slide 20
e- flux@wall vs. intensity, 25 ns spacing, ‘best’ model
R=0.5
calculation for 1 batch
dmax=1.7
dmax=1.5
dmax=1.3
dmax=1.1
LHC vacuum pressure with electron cloud
17 hr running at 3 mA/m gives CO pressure corresponding to
100-hr beam lifetime (N. Hilleret, LHC MAC December 2004)
Presentation to LHC MAC 10 June 2005

## Slide 21
dmax=1.7
dmax=1.5
dmax=1.3
dmax=1.1
nominal Nb
stability limit
at injection
the challenge is to decrease dmax to 1.3 with a stable beam
nominal filling pattern
top energy
Presentation to LHC MAC 10 June 2005

## Slide 22
electron cloud in the LSS
electron-cloud simulations at 25-ns bunch spacing for the two-beam IR sections were performed by Giovanni Rumolo, Adriana Rossi and Frank Zimmermann in the period 1999-2002 to specify the acceptable maximum secondary emission yield in this region
nominal LHC beam & SEY values between 1.1 and 1.4 had been considered; see
F. Zimmermann: Electron-Cloud Simulations for the LHC Straight Sections, LHC Project Note 201, 1999;
Rossi, G. Rumolo, F. Zimmermann: A Simulation Study of the Electron Cloud in the Experimental Regions of LHC, Proceedings ECLOUD’02 workshop, Geneva, Yellow Report CERN-2002-001, pp. 123).
new simulations for much higher SEY are being launched

## Slide 23: early preliminary LHC findings
at 50-ns spacing strong evidence for large electron
  cloud build up in warm and cold sections
cold sections are of bigger concern
both heat load & instability in 3rd and 4th train
indicate SEY dmax~2.5&R=0.5 or R~2.2&R=1.0
in the arcs
  av. e-cloud density ~6x1011 m-3 (from Q’ effect)
  expected tune shift: DQ~rpreCb/(2g)~ 0.0025
  new simulations for LSS and more simulations for
    arcs are in progress
    determine R from memory effect between trains

## Slide 24: ongoing, planned & proposed studies

## Slide 25: ECLOUD simulations (Humberto, Octavio)
SPS benchmark – ONGOING (Octavio)
  simulations for 25, 50 and 75 ns; MBB, MBA and detectors, beam parameters (?)
  consistency check with 2010 SPS data (question by M. Jimenez)
  find d,R,e for SPS
LHC LSS at 150 ns – PLANNED (Humberto)
  3 locations &fields at about 59 m from IP1 with both beams present
  simulate passage of 17 bunches with known time separation
  effect of solenoid ; + generic study: dependence on LSS aperture
memory effect in LSSs at 50 ns – PLANNED (Octavio?)
  simulations for IR3 as a start, Nb scan
  need memory data from other IRs; find d,R,e ; triplet heat load (L8)
  other LSS simulations for different train patterns (scrubbing), common sections
simulations for arc – ONGOING (Humberto)
  heat load, central density (instability), flux on wall (scrubbing); find d,R,e
  dependence on beam size & bunch length

## Slide 26: ECLOUD simulations (Humberto, Octavio)
multi-bunch wake field and CB instability rise times
  including combined coupled/single-bunch effects
  wake field from ECLOUD (see nice study by Daniel a few years back)
scrubbing scenario for 2011
  simulations for 50 and 75 ns
  determine stable regions in d,R,e space for different beams ; LSS solenoid effect
  iterate with expected evolution of d,R,e as a function of flux
  effect of satellite bunches – STARTED (Humberto)
scrubbing optimization for 2011
  simulations for 50 and 75 ns to determine map coefficients
  use map to optimize fill pattern and generalize map approach to find optimum scrubbing stages
  help from Theo Demma and/or Ubaldo Iriso?
  extended LHC forecast – PLANNED (Humberto)
  simulations for larger values of d

## Slide 27
2/11/2010
8x1011
m-3
arc dipole
dmax=2.5
R=0.5
1 nTorr
Nb=1.2x1011
~instability
threshold
arc dipole
dmax=2.4
R=0.5
1 nTorr
Nb=1.2x1011
1010 m-3
LHC at injection: 4x24 bunch pattern (+3x37 missing bunches)
emittance growth observation
F. Roncarolo
for dmax=2.4, R=0.5:
no multipacting
central
cloud
density
Humberto
with R=0.5,
multipacting
for dmax≥2.5

## Slide 28
8x1011
m-3
arc dipole
dmax=2.5
R=0.5
1 nTorr
Nb=1.2x1011
~instability
threshold
arc dipole
dmax=2.5
R=0.5
10 nTorr
Nb=1.2x1011
7x1012
m-3
~instability
threshold
~instability
threshold
LHC at injection: 4x24 bunch pattern (+3x37 missing bunches)
1.0x1013
m-3
5x1012
m-3
arc dipole
dmax=2.1
R=1.0
1 nTorr
Nb=1.2x1011
~instability
threshold
central cloud density
Humberto
arc dipole
dmax=2.2
R=1.0
1 nTorr
Nb=1.2x1011

## Slide 29
70
mW/m
/bunch
arc dipole
dmax=2.5
R=0.5
1 nTorr
Nb=1.2x1011
arc dipole
dmax=2.5
R=0.5
10 nTorr
Nb=1.2x1011
arc dipole
dmax=2.5
R=1.0
1 nTorr
Nb=1.2x1011
LHC at injection: 4x24 bunch pattern (+3x37 missing bunches)
arc dipole
dmax=2.4
R=1.0
1 nTorr
Nb=1.2x1011
700
mW/m
/bunch
3 W/m
/bunch
3.5 W/m
/bunch
heat load
Humberto

## Slide 30
dmax | Nb | P [nTorr] | R | dP/ds [mW/m] | total e- flux [mA/m] | e- flux > 30 eV [mA/m]
2.4 | 1.2x1011 | 1 | 0.5 | 0.001 | 0.034 | 0.011
2.5 | 1.2x1011 | 1 | 0.5 | 0.18 | 0.697 | 0.239
2.5 | 1.2x1011 | 10 | 0.5 | 3.3 | 12.3 | 4.34
2.5 | 1.2x1011 | 1 | 1.0 | 61 | 268 | 69.8
2.4 | 1.2x1011 | 1 | 1.0 | 46 | 200 | 52.7
2.5 | 1.0x1011 | 1 | 0.5 | 0.44 | 2.1 | 0.71
2.5 (top!) | 1.2x1011 | 1 | 0.5 | 59 | 356 | 93.8
simulation results for 4x24 bunches [at injection]
(1.85 ms spacing between batches)
30 days continuous running at 70 mA/m gives CO pressure
corresponding to 100-hr beam lifetime (N. Hilleret, LHC MAC Dec.2004);
2 days continuous running at 70 mA/m gives 1 mC/mm2 !
H. Maury Cuna

## Slide 31
Octavio
strip detector (~MBB)
threshold much lower
than for LHC;
check MBA chamber
LHC, R=0.5 (Humberto)
LHC, R=1.0 (Humberto)

## Slide 32
24.3 mm
47.15 mm
24.3 mm
47.15 mm
70.0 mm
70.0 mm
bending field, 2.025 T
sx= 0.9 mm; sy= 0.4 mm; sz= 11.8 cm; emax= 230
Octavio
difference SPS - LHC? (chamber shape? chamber radius?)
Bs [ns] | R | pipe shape | hx[m] | hy,hz [m] | pressure [nTorr] | onset
50 | 0.7 | Elliptical | 0.07 | 0.0243 | 9 | 1.7
50 | 0.7 | Elliptical | 0.07 | 0.04715 | 9 | 1.3
50 | 0.7 | Round | 0.07 | 0.07 | 9 | 1.5
50 | 0.7 | Elliptical | 0.04715 | 0.0243 | 9 | 1.7
50 | 0.7 | Round | 0.0243 | 0.0243 | 9 | 1.6

## Slide 33
R
dmax

## Slide 34: HEADTAIL simulations (Tatiana, Kevin?, Giovanni? Elena? )
tune shift with stripes (question by Stephane Fartoukh)
  include proper chamber boundaries with image current; analytical estimate?
  see APAC’01 paper with Ohmi and Sam H., and Chamonix 2001 paper
single-bunch instability threshold and growth rates
  simulations for 0.45, 3.5, and 7 TeV; parameters to be defined
e-cloud induced energy loss & phase shift
  old studies by G. Rumolo & F.Z., USC group, A. Novokhatski
effect of transverse offset (question by Wolfgang Hofle)
  include proper chamber boundaries with image current and reasonable electron reflection/secondary emission
  start with SPS ; - some analytical estimate could also be developed
incoherent effects - collaboration with Giuliano Franchetti (?)
interplay with beam-beam
  old (2002) study by Ohmi and Chao in ECLOUD02 proceedings

## Slide 35: experiments
need to collect all relevant data (bunch length, emittance, aperture,…)
propose additional experiments