## Slide 1
DeltaPhi | Ap-FFT* | Matlab | Sussix
90 | 0.8e-6 | 2.0e-4 | 5e-3
180 | 1.0e-6 | 4.6e-4 | 4.2e-4
270 | 3.1e-6 | 7.8e-4 | 4.8e-3
DeltaPhi | Ap-FFT | Matlab | Sussix
90 | 1e-2 | 9e-3 | 6e-3
180 | 9.5e-3 | 2.1e-2 | 2.8e-2
270 | 6e-3 | 1.7e-2 | 1.9e-2
Phase advance accuracy (rms value)
No noise case
10% Gaussian noise
* “NEW METHOD OF ESTIMATION OF PHASE ,AMPLITUDE, AND FREQUENCY BASED ON ALL PHASE FFT SPECTRUM ANALYSIS” Huang Xiaohong, Wang Zhaohua, Hou Guoqiang.
Comparing the phase accuracy got by different FFT codes, All-phase FFT (see article on footnote), Matlab FFT, and SUSSIX-FFT, in case of ideal sinusoidal signals with phase advance typical for SPS FODO lattice, and adding additive gaussian noise.

## Slide 2
DeltaPhi | x1 | x10 | x20
90 | 4.1e-4 | 4.3e-3 | 9.6e-3
180 | 2.3e-4 | 2.5e-3 | 5.3e-3
270 | 1.9e-4 | 2.2e-3 | 4.4e-3
Phase advance accuracy on 90deg lattice (rms value)
Methodology:
1- Put 1 Impedance source (MKPA.11936)
2- Track HEADTAIL multi-kick code and get phase advances with Matlab.
3- Do the same increasing the wake field strength with factors [x1 x10 x20]
Phase advance rms values for different phase advances and different impedance strength
Obs: I measured M=var(ΣX)=Σvar(X)=N var(X) in case of N indipendent measurements -> std(X)=sqrt(var(X))=sqrt(M/N).

## Slide 3
DeltaPhi | rms
67 | 4.0e-4
133 | 4.7e-4
200 | 8.7e-5
Phase advance accuracy on 67deg (low γ) lattice (rms value)
Methodology:
1- Put 1 Impedance source (MKPA.11931)
2- Track HEADTAIL multi-kick code and get phase advances with Matlab.

## Slide 4
DeltaPhi | Ap-FFT | Matlab | Sussix
90 | 1e-3 | 1e-3 | 1e-7
180 | 1e-3 | 1e-3 | 1e-7
207 | 1e-3 | 1e-3 | 1e-7
DeltaPhi | Ap-FFT | Matlab | Sussix
90 | 1e-3 | 1e-3 | 5e-6
180 | 1e-3 | 1e-3 | 5e-6
270 | 1e-3 | 1e-3 | 5e-6
Frequency accuracy (rms value)
No noise case
10% Gaussian noise
Comparing the frequency accuracy got by different FFT codes, in case of ideal and noisy sinusoidal signals with phase advance typical for SPS FODO lattice, as done before for the phase.

## Slide 5
Using Ap-FFT
Using Matlab-FFT
Some quick comparison: using ap-FFT for simulation data increase the accuracy in phase determination for the tracked signals. This permits to gain a better resolution in reconstruction (avoids peaks forest at the end).
Example of localization with a low gamma lattice using ap-FFTand matlab FFT.