## Slide 1: Measurement opportunities with the LHC transverse damper
W. Hofle, D. Valuch

## Slide 2: LHC transverse damper (ADT)
Transverse damping systems help to damp the transverse beam oscillations
  Transverse injection errors
  Damping of coupled bunch instabilities
Two stripline pickups at
point 4, magnets Q7 and Q9
Electrostatic deflectors,
bandwidth 3kHz – 20MHz

## Slide 3: ADT layout in the machine

## Slide 4: Observation modes
Circular buffer
  Buffer constantly records data
  Recording stopped by software trigger, hardware trigger or a timing event
  Hardware initiated freeze can be beam-synchronous
  Release by FESA after the buffer is read out
  Transfer of one 256k buffer takes about 1 second

## Slide 5: Observation modes
Single shot buffer
  Recording triggered by software trigger, hardware trigger or a timing event
  Recording stops when the buffer is full
  Hardware initiated freeze can be beam-synchronous
  Release by FESA after the buffer is read out

## Slide 6: Observation triggers
Various trigger methods allow to obtain:
  Synchronized data for Q7/Q9
  Independent data for each pickup

## Slide 7: Observation data
entire ADT works with 16 bit integer data
some calculations are done in 32 bit precision, selecting the 16 relevant bits for the result
system records 18 bits of data, 16 are available from FESA
full precision data retrieval (by setting a control bit)
stamped data retrieval (standard mode)

## Slide 8: Beam Position module (Bpos)
Calculates normalized beam position bunch by bunch, independent of intensity
16 bit ADCs

## Slide 9: Beam Position module (Bpos)
Normalized bunch position calculation
angle fDS determined during
setting-up, different settings required for
different gains in pre-amplification chain

## Slide 10: Normalized position calculation (1)
The following 4 quantities are digitized:
The angles refer to the phase relation of the 400 MHz RF with respect to the 400 MHz component of the beam signal on the mixer
The normalised position can be computed from
The normalised position can be computed from with the sign chosen accordingly from the signs of the 4 components digitized, in practice this was tried using a cordic algorithm giving also the sign but this method was abondoned as the presence of noise on the signals leads to a wrongly chosen sign for small signals (beam centered), effectively leading to non gaussian distribution of the normalised position with two maxima at opposite signs

## Slide 11: Normalized position calculation (2)
A different algorithm is used using the same quantities
but not needing a square root
During the setting-up the rotation angle is determined and one of the signals rotated so the two I/Q basis match and the subsequent computation gives the correct normalised position and fixes the sign correctly for all cases

## Slide 12: Normalized position calculation (3)
all computations are done in fixed point arithmetics on an FPGA
system can saturate (ADC)
level of saturation depends on the beam intensity and on the bunch length as the system uses the 400 MHz beam component
saturation can occur on one of the four signals only  complicated dependence of normalized position
saturation may be seen at injection (large oscillations) or at the start of the ramp (short bunches)
estimated saturation at 2 mm and 1.2x1011 and 1 ns bunch length
precision: estimated at 2 mm rms

## Slide 13: Calibration factors (steps/mm)
ADT pick-ups calibrated with orbit bumps and orbit BPMs
Available different sets of calibration data for different gains of pre-amplification

## Slide 14: Beam Position module (Bpos)
Available data, 4 buffers of 256k samples :
Multiturn app accesses this memory

## Slide 15: Beam Position module (Bpos)
Available data, 4 buffers of 256k samples, 16 bit unstamped data
  73 turns at full rate
  262144 turns in 1 bunch mode
  131072 turns in 2 bunch mode
  65536 turns in 4 bunch mode
  32768 turns in 8 bunch mode
Being implemented
  262144 sample-turns in bunch mask mode (not tested yet)

## Slide 16: Digital Signal Processing Unit (DSPU)
Damper feedback loop, Injection + Abort gap cleaning
Works bunch by bunch (40 MHz rate)

## Slide 17: Digital Signal Processing Unit (DSPU)
Available data, 8 buffers of 256k samples + 2x 8192 turn memory for injection oscillations
  Data size 73 turns at full rate
  14-bit frev stamped data
Data interesting for observation

## Slide 18: Digital Signal Processing Unit (DSPU)
Majority of the available memory space sits there idle most of time
Provided sufficient resources are available the observation could be modified into: