## Slide 1: Studies of impedance effects for a composite beam pipe for the experimental areas
Request from M. Galilee, G. Schneider (TE/VSC)

## Slide 2: Context
The vacuum group is looking at the opportunity to replace the current LHC experimental beam pipes by composites: titanium (or Aluminum) + carbon-carbon
NEG coating of 3 micron would still be put on the inside
Reason: Beryllium (as now installed in the inner chamber) would be by far the best material (very high Young’s modulus and low atomic number). However cost (150,000 CHF/m!!!) and more importantly toxicity are calling for other options.
Current layout (for 50 mm diameter):
Vacuum(25mm) /NEG (3μm)
/Cu(0.2mm)
/SS(1mm)
/vacuum
Proposed layout 1
Vacuum /NEG(3μm) /CC(1% diam0.5mm)
/Ti (0.3 mm or Al (0.4 mm))
/vacuum
Proposed layout 1
Vacuum /NEG(3μm) /Ti (0.3 mm or Al (0.4 mm))
/CC(1% diam 0.5mm)
/vacuum

## Slide 3: Material parameters used for the resistive wall impedance
• Beryllium:
– Resistivity: 4.24 10-8 Ω.m (from specifications)
– Permittivity: 1
• Carbon-carbon composite:
– Resistivity: 16 10-6 Ω.m (from specifications)
– Permittivity: 1
• NEG:
– Resistivity: 2.5 10-5 Ω.m (David Seebacher, F. Caspers, NEG properties in the microwave range, SPSU Meeting, 17th February, CERN)
– Permittivity: 10
• Titanium:
– Resistivity: 0.42 10-6 Ω.m (from specifications)
– Permittivity: 1
• Aluminum:
– Resistivity: 16 10-6 Ω.m (from specifications)
– Permittivity: 1

## Slide 4: Resistive wall models
Two models used here:
  Exact multilayer analytical formula for an axisymmetric geometry (assumptions: linear materials, infinite length i.e. no side effects). Implemented in a Mathematica code (ReWall – http://impedance.web.cern.ch/impedance/Codes/ReWall/ReWall_to_date.zip)
  Classic thick wall formula (Chao’s book) giving a simple impedance formula for a resistive beam pipe, valid at “intermediate” frequencies:
Longitudinal impedance:
Transverse impedance:
with L the length of the element, b its radius, s the wall conductivity, m0 the vacuum permeability, Z0= m0 c the vacuum impedance (c=speed of light), and w the angular frequency.

## Slide 5: Power loss due to the impedance
General expression for any impedance: loss is a function of the real part of the longitudinal impedance and of the bunch spectrum l(w) (=line density in frequency domain, here for a parabolic bunch):
with f0=w0 /2p the revolution frequency, M the number of bunches and e the electron charge.
For a classic resistive wall impedance and a parabolic line density, we can get an analytic formula:
for a bunch of total length 4sz=4stc (in meters), L=26658.883 being the circumference of the LHC and Lelem the length of the element considered for the impedance (here 7.1 m).
Power loss per unit length :
G. Rumolo, USPAS 2009

## Slide 6: Results for 1 layer
1st layer | 2nd layer | Im(Zeff (trans)) in kOhm/m | Im(Zeff /n) (long) in Ohm | Power loss
Be | - | 6 | 2.7e-4 | 0.7 W/m
Ti | - | 18 | 7e-4 | 2 W/m
Al | - | 4.8 | 2.4e-4 | 0.5 W/m
Carbon | - | 113 | 4e-3 | 13 W/m
NEG | - | 142 | 5e-3 | 16 W/m
Cu | - | 4 | 2e-4 | 0.4 W/m
Total for LHC |  | ~2400 | ~0.09 | 
Parameters: 25 mm radius, 160m length, 2*2808 bunches, 450 GeV, 1.15e11p/b, 1.4 ns
large contribution for the carbon pipe (5 % of the total longitudinal impedance)

## Slide 7: 1 and 2 layers
1st layer | 2nd layer | Im(Zeff (trans)) in kOhm/m | Im(Zeff /n) (long) in Ohm | Power loss
Cu | - | 4 | 2e-4 | 0.4 W/m
Cu (0.2mm) | Stainless steel | 4 | 2e-4 | 0.4 W/m
NEG (3 mic) | Cu | 7 | 5e-4 | 0.4 W/m
Total for LHC |  | ~2400 | ~0.09 | 

## Slide 8: Difference between single and more layers
difference only well below 1 MHz  explains similar results with 1 and 2 layers

## Slide 9: Results for 2 layers
1st layer | 2nd layer | Im(Zeff (trans)) in kOhm/m | Im(Zeff /n) (long) in Ohm | Power loss
Be (inf) | - | 5.92 | 2.7e-4 | 0.7 W/m
Be (0.8mm) | vacuum | 5.91 | 2.7e-4 | 0.7 W/m
NEG (3 μm) | Be | 9.60 | 5.4e-4 | 0.7 W/m
Carbon (inf) | - | 113 | 4e-3 | 13 W/m
Carbon (0.5mm) | Ti | 113 | 4e-3 | 12 W/m
NEG(3 μm) | CC | 115 | 4e-3 | 13 W/m
Ti | - | 18 | 7e-4 | 2 W/m
Ti (0.3mm) | CC | 18 | 7e-4 | 2 W/m
NEG(3 μm) | Ti | 22 | 9.7e-4 | 2 W/m
Total for LHC |  | ~2400 | ~0.09 | 
Parameters: 25 mm radius, 160m length, 2*2808 bunches, 450 GeV, 1.15e11p/b, 1.4 ns
 Apart from NEG, all other inner materials block most of the fields inside them

## Slide 10: Results for 1 carbon layer
radius | Im(Zeff (trans)) in kOhm/m | Im(Zeff /n) (long) in Ohm | Power loss
25mm | 113 | 4e-3 | 13 W/m
50mm | 14 | 2e-3 | 6 W/m
100mm | 2 | 1e-3 | 3 W/m
200mm | 0.2 | 0.5e-3 | 1.6 W/m
Total for LHC | ~2400 | ~0.09 | 
Parameters: varying radii, 160m length, 2*2808 bunches, 450 GeV, 1.15e11p/b, 1.4 ns
 In agreement with classical thick wall theory

## Slide 11: Results for 1 carbon layer for flat top
Energy | Bunch length 4 sigma | Im(Zeff (trans)) in kOhm/m | Im(Zeff /n) (long) in Ohm | Power loss
450 GeV | 1.4 ns | 113 | 4e-3 | 13 W/m
3.5 TeV | 0.8 ns | 86 | 2.9e-3 | 30 W/m
7TeV | 1 ns | 96 | 3.3e-3 | 21 W/m
Total for LHC |  | ~2400 | ~0.09 | 
Parameters: 25 mm, 160m length, 2*2808 bunches, varying energies, 1.15e11p/b
large power losses (mainly due to the reducing bunch length)

## Slide 12: Preliminary conclusions
The solution with carbon-carbon composite on the inner part of the beam pipe would increase the total longitudinal impedance of the machine by 5% (if all 160m are at 25mm radius)
The large power losses (10 to 30 W/m) may require cooling.
The 3 micron NEG coating does not affect the power loss but increases significantly the real tune shifts (both longitudinal and transverse).