## Slide 1: TCTP the CST side
F. Caspers, H. Day, A. Grudiev, E. Metral, B. Salvant
Acknowledgments: R. Assmann, A. Dallocchio, L. Gentini, C. Zannini
Impedance Meeting 17 Oct 2011

## Slide 2: Issues to decide
What do we do with the gap above the jaws ?
Should we act on the longitudinal modes generated by the transition region?

## Slide 3: Options on the table
Current design (gap opened and ferrite)
No ferrite but gap still opened
RF contacts to close the gap

## Slide 4
Open structure (with pec, no ferrite)
Closed structure (simulates ideal RF contacts)
Open structure (with ferrite)
Pros:
No friction
Transverse modes damped
longitudinal modes also damped
Cons:
Low frequency transverse modes
Low frequency impedance
increase
- Small gaps are predicted to generate large intensity effects
- Risk with material model and specifications
Pros:
No friction
model well defined
Cons:
Low frequency transverse modes
large power loss
- Small gaps are predicted to generate large intensity effects
Pros:
No transverse modes
- Solution for phase 1 works
Cons:
Contacts not well defined
solution involves fingers seen directly by the beam
longitudinal modes are not damped

## Slide 5
new rf system
  Longer RF fingers must be
  installed on the axis area.
Longer RF finger

## Slide 6
new rf system
Groove on the screen for RF fingers

## Slide 7: Effect of ferrite (2 mm half gap case)
- Previous simulations were performed with only 10 m of wake (limit for acceptable simulation time)
On the new super PC, we could try 60 m wake, and effect of ferrite is now clear: frequency decreases and all transverse modes are damped. However, low frequency (<100 MHz ) impedance increases (factor 2).
and the longitudinal modes?

## Slide 8: Effect of ferrite on longitudinal modes
Ferrites seem to help significantly in the longitudinal plane too.

## Slide 9: Eigenmode simulations (without lossy material, all copper)

## Slide 10: Small plate gap 1.5mm (jaw half gap 5 mm)
frequency | Rs (dy=1mm) | Rs (dy=0mm) | Q (copper) | Power loss
95 | 30 | 1 | 752 | 
196 | 18 | 1 | 868 | 
301 | 0 | 3 | 1116 | 
317 | 5 | 0 | 2821 | 
382 | 34 | 7 | 3403 | 
390 | 6 | 3 | 3383 | 
411 | 96 | 96 | 2769 | 34 W
416 | 8 | 6 | 1095 | 
440 | 211 | 189 | 2201 | 70 W
473 | 2 | 0 | 2145 | 
505 | 10 | 29 | 2878 | 
518 | 17 | 20 | 3931 | 
529 | 1 | 1 | 1059 | 
554 | 56 | 55 | 1541 | 
613 | 1 | 4 | 2963 | 
637 | 166 | 165 | 2076 | 32 W
643 | 1 | 0 | 1227 | 
Transverse modes but also large longitudinal modes

## Slide 11: With cone
frequency | Rs (dy=1mm) | Rs (dy=0mm) | Q (copper) | 
117 | 41 | 0 | 1833 | 
132 | 1 | 0 | 2072 | 
236 | 76 | 0 | 2578 | 
261 | 3 | 0 | 2922 | 
334 | 2 | 0 | 6602 | 
359 | 81 | 0 | 3135 | 
391 | 4 | 0 | 3581 | 
405 | 3 | 0 | 5230 | 
482 | 58 | 0 | 3627 | 
504 | 22 | 0 | 4744 | 
Low frequency longitudinal modes are suppressed if the transition RF fingers are replaced by a taper

## Slide 12: Closed (half gap 5 mm)
frequency | Rs (dy=1mm) | Rs (dy=0mm) | Q (copper) | Power loss
263 | 1 | 1 | 2941 | 
392 | 2 | 2 | 3564 | 
518 | 5 | 5 | 4036 | 1 W
641 | 11 | 11 | 4405 | 2 W
760 | 31 | 31 | 4684 | 4 W
869 | 10 | 10 | 5060 | 
869 | 144 | 144 | 4903 | 12 W
953 | 410 | 355 | 5450 | 23 W
959 | 754 | 813 | 5063 | 42 W
980 | 274 | 263 | 4985 | 13 W
994 | 81 | 104 | 5246 | 
1020 | 130 | 112 | 5273 | 
1023 | 2267 | 2275 | 5101 | 92 W
1047 | 92 | 82 | 5914 | 
1048 | 38 | 33 | 5164 | 
1074 | 36 | 9 | 6364 | 
1110 | 1711 | 1695 | 5360 | 46 W
Closed structure kills all transverse modes, but large longitudinal modes remain

## Slide 13: Small plate gap 1.5mm (half gap 3.6 mm)
frequency | Rs (dy=1mm) | Rs (dy=0mm) | Q (copper) | Power loss
94 | 54 | 0 | 801 | 
194 | 30 | 1 | 904 | 
382 | 32 | 4 | 3813 | 
481 | 383 | 341 | 2243 | 117 W
518 | 24 | 27 | 3942 | 
527 | 36 | 21 | 1319 | 9 W
533 | 65 | 89 | 1563 | 
640 | 33 | 36 | 4210 | 
677 | 28 | 26 | 1483 | 
757 | 128 | 130 | 3242 | 16 W
772 | 58 | 56 | 1677 | 
847 | 20 | 4 | 2299 | 
860 | 307 | 311 | 2226 | 26 W
877 | 28 | 27 | 2349 | 
948 | 921 | 918 | 2997 | 54 W
957 | 51 | 17 | 2577 | 
970 | 17 | 47 | 4974 | 
983 | 63 | 55 | 2117 | 
992 | 68 | 209 | 2321 | 
1023 | 6 | 1 | 3502 | 
Modes shunt impedance is multiplied by a factor ~2 if half gap goes from 5 mm (TCTP) to 3.6 mm (TCSG6)

## Slide 14: Stability diagram (7 TeV)
4 TCTP at 5 mm at 635m (larger plate gap, without ferrite)
Rs=45e3*4*635/avbeta; %in Ohm/m
Q=1790;
fres=112e6; % in Hz
clight=299792458;
gamma=7460.52;
betab=sqrt(1-1/gamma^2);
circum=26658.883;
taub=1e-9; %in s
fs=23; % Hz
f0=betab*clight/circum;
tunes=fs/f0;
Nb=1.15e11;
tune=64.31; %in H
%tunes=0.002;
%tunes=0.00374652;
particle='proton';
chroma=0;
alphap=3.225e-4;
M=3564;
mmax=0;
First transverse mode damped by 3 A in octupoles

## Slide 15: Conclusions
New design already generates very large intensity effects below 3 mm half gap (due to new taper).
Open plate gap without ferrite seems unacceptable from power loss point of view.
Both other choices present risks from impedance point of view:
  RF fingers:
    Impedance of fingers seen by the beam?
    no damping of longitudinal modes
    Contact resistance not known
  ferrite:
    Decreasing the gap is not an option
    Increase of low frequency transverse impedance (before 100 MHz)
    Low frequency transverse modes are damped but present
    Problem of knowing exactly the ferrite material and its specs
It will be difficult to guarantee that the new design is at least as good as the old one…

## Slide 16: What would be left to do?
See Hugo’s talk for eigenmode simulations of ferrite damping
Go higher than 1.1 GHz to check all the other modes
Use real bunch spectrum

## Slide 17: Power losses calculations
If we assume the mode frequency overlaps with one of the beam harmonics (conservative approach)
With the parameters of the LHC nominal beam
  nominal bunch charge after splitting q = 18.4 nC (1.15 e11 p/b)
  bunch spacing = 25 ns (worst case scenario)
  smallest nominal RMS bunch length = 7.5 cm
  Rs is the shunt impedance (linac convention)
  z is the rms bunch length in m
Remarks: Q is obtained with the formula
with W= total stored energy
(W=1J in eigenmode)
Perturbation method id used to obtain the Q and R for stainless steel.