## Slide 1
TCTVB-VMTSA-TCDD area
Xrays at 4L2
V. Baglin (8/11/11)
CERN TE-VSC, Geneva
X-Rays made by A. Vidal (TE/VSC) and A-M Piguiet (EN/MME)

## Slide 2
Layout LSS2 : A4L2
TCDD
LSS2L :
  TCTVB
  TCDD
  VAB
  BPMSX
  D1L2
D1L2
VPIA.A151.4L2.X
VGPB.120.4L2.X
VAMTF.A4L2.X
DCUM = 3259.3524

## Slide 3
VMTSA son of VAMTF.A4L2.X
LHCVMTSA0001
Horizontal ellipse 180/70
Left side
Right side

## Slide 4
X-rays the 10-5-2011, DCUM 3259
Left side
Top view (xray from top to bottom)
a)Slight deformation of
RF finger.
b)No metallic noise due to loose spring
Use as IS
a
b

## Slide 5
X-rays the 10-5-2011, DCUM 3259
Right side
Top view (xray from top to bottom)
b) No metallic noise due to loose spring
Conform
b

## Slide 6
X-rays the 7-11-2011, DCUM 3259
Left side
Top view (xray from top to bottom)
a)Strong deformation of
RF finger.
b) Metallic noise due to loose spring when hitting vacuum chamber
Non Conform
a
b

## Slide 7
X-rays the 7-11-2011, DCUM 3259
Left side
Side view (xray from corridor to QRL)
b) Metallic noise due to loose spring when hitting vacuum chamber
c) RF fingers falling due to broken spring
Non Conform
c
b
Spring was broken between May and November 2011
Probably as a consequence of irradiation

## Slide 8
X-rays the 7-11-2011, DCUM 3259
Photo to come
Right side
X-ray done also
RF fingers and spring are
Conform

## Slide 9
Other similar regions in LHC: Layout LSS2-LSS8
https://lhc-div-miwg.web.cern.ch/lhc-div-miwg/Main_Pages/new_frame%20miwg_icl.htm
TCDD
TCLIA
LSS2L :
  TCTVB
  TCDD
  VAB
  BPMSX
  D1L2
LSS2R :
  D1R2
  BPMSX
  VAB
  VCTCQ
  TCTVB
  TCLIA
LSS8L :
  TCLIA
  TCTVB
  VCTCF
  VAB
  BPMSX
  D1L8
LSS8R :
  D1R8
  BPMSX
  VAB
  TCDDM
  TCTVB
TCLIA
D1L2
D1R2
D1R8
D1L8
VPIA.A173.4L8.X
VPIA.A147.4R8.X
VPIA.A151.4L2.X
VPIA.A170.4R2.X
VGPB.120.4L2.X
VGPB.120.4L8.X
VGPB.120.4R2.X
VGPB.120.4R8.X