## Slide 1: Overview of HOM Damping in PEP-II
Mauro Pivi, SLAC while at CERN
ICE Meeting, CERN
April 18, 2012

## Slide 2
S. NovoKhatski
On behalf of

## Slide 3
Linac and PEP-II

## Slide 4: Layout of the PEP-II Ring
9 GeV
3.1 GeV

## Slide 5: Luminosity and electromagnetic fields
PEP-II: high current beams of very short bunches to achieve very high luminosity
These beams carry high intensity electromagnetic fields.
Electric field at the beam pipe wall
Fields near a sharp metal corner may exceed the breakdown threshold
HOM power scales as:

## Slide 6: Bunch field spectrum
Field spectrum goes to higher frequency with shorter bunches exponentially
Beam spectrum (12 mm bunch)
Bunch spacing resonances
Bunch spacing

## Slide 7: Small Gap, Breakdowns and Temperature Oscillations
Very small gaps are the source of high intensity wake fields causing electric breakdowns
Breakdowns

## Slide 8: Wake field Evidence from PEP-II
Shielded fingers of some vacuum valves were destroyed by breakdowns of intensive HOMs excited in the valve cavity.

## Slide 9: HOM leaking from TSP heater connector
HOM spectrum from
Spectrum analyzer
antenna
Wake fields can leave the vacuum chamber through heating wires of Titanium Sublimation Pumps (TSP)

## Slide 10: HOMs go through RF screens
antenna
RF spectrum
RF screens

## Slide 11: A gap ring may be a reason for the beam instability
Breakdowns traces

## Slide 12: Fast Instability and vacuum spikes
abort
LER
vacuum

## Slide 13
Wake fields transfer energy to resonance HOMs excited in the closed volumes of shielded bellows.
Simulated magnetic energy density (MAFIA)
Temperature ©

## Slide 14: Main HOM Source are Collimators
MAC Review

## Slide 15: What we can do
There is only one way:
extract HOM power from the beam pipe by specially designed water-cooled RF absorbers, before HOM reach sensitive components

## Slide 16
S. Weathersby, SLAC
HOM absorber in PEP-II arc antechamber

## Slide 17
HOM damping following absorber installation
Temperature reduction at TSP feed-through downstream location

## Slide 18
S. Weathersby, SLAC
Existing Q2 bellow with tiles fully exposed to beam
HOM 10 kW deposited in Q2 bellow area
Bellows in the Interaction Region area: Q2
Absorption spectra analysis. High monopole value

## Slide 19
Bellows in the Interaction Region area: Q2
Spectral mode analysis for new bellow. Reduced monopole.
New Q2 bellow, coupling slots and ceralloy tiles behind
Absorption vs slot length for dipole and quadrupole modes
S. Weathersby, SLAC

## Slide 20
New Q2 bellow
Old Q2 bellow

## Slide 21
New optimized high efficiency absorbing device
Long coupling slots, and tiles brazed to copper with cooling line, dimensions in inches
J.Seeman, S. Novokhatski, S. Weathersby, N. Kurita and N. Reeck
54%
88%
89%

## Slide 22
Developed high efficiency HOMs absorbers for different cross sections and installed 25 in the rings

## Slide 23
Properties of ceramic tiles

## Slide 24
Collective Effects test set-up (no 1) in PEP-II: controlling HOM
sample surface exposed to SR and to electron cloud
PEP-II LER side
Samples moved by manipulators to face the interior of the vacuum chamber
Must avoid beam HOM into the 2 manipulators: assure perfect contact of the samples to the chamber wall, together with the use of RF seal springs
Cu-Be Ag coated RF seal

## Slide 25
Collective Effects test set-up (no 3) in PEP-II: controlling HOM
Holes in the wall to measure electron cloud current
Need to avoid propagation of HOM through holes: holes size designed to damp beam RF
OUTCOME: No HOM issues in electron cloud set-ups. Smooth operations of PEP-II + new break-through findings from tests.
Chicane inner view
Chamber inner view
Chicane installed in PEP-II

## Slide 26
Summary
  As bunch currents increase, became clear that wake field effects have been underestimated during machine design
  Important understanding of HOMs in accelerators achieved
  Collimators identified as source of HOMs heating
  Developed devices to selectively couple dipole and quadrupole modes and discourage monopole mode coupling
  PEP-II collider ended at nearly twice the design current and 4X the design luminosity.
    - Beam current = 3 A and L = 1.2  1034 cm-2 s-1
  HOM have been a limitation to further increase current
26

## Slide 27: Main High Order Modes (HOM) Effects
  Heating of vacuum elements
    Temperature and vacuum rise
      Deformations and vacuum leaks
      Decreasing pumping speed
  Breakdowns and multipacting
      Vacuum leaks
      Melting thin shielded fingers
      Longitudinal instabilities
  Electromagnetic waves outside vacuum chamber
      Interaction with high sensitive electronics

## Slide 28: Examples from PEP-II
A very small gap in a vacuum chamber is the source of high intensity wake fields, which cause electric breakdowns

## Slide 29: HOMs with transverse components
Wake fields, which have transverse components may penetrate through small slits of shielded fingers to vacuum valves volumes and excite high voltage resonance fields, which may destroy the fingers

## Slide 30: Wake fields outside
Wake fields can go outside the vacuum chamber through heating wires of Titanium Sublimation Pumps (TSP).

## Slide 31: Wake fields
Other possibilities for wakes to go outside is to escaped from the vacuum pumps through RF screens

## Slide 32: Temperature raise
Propagating in the vacuum chamber wake fields may transfer energy to resonance High Order Modes (HOMs) excited in the closed volumes of shielded bellows.
Main effect is the temperature rise