## Slide 1: Collective effects in the SPS and LHC (longitudinal plane)
T. Argyropoulos, T. Bohl, J. E. Muller,
E. Shaposhnikova + many other colleagues

## Slide 2: Main intensity limitation in the SPS: longitudinal instability during the ramp
Small injected bunches are unstable on the 450 GeV flat top (50 ns beam)
Very low intensity threshold - 2x1010/bunch (at the end of the ramp), reduces with energy
Depends on single bunch and total beam intensity
Bunches with smaller longitudinal emittance are more unstable

## Slide 3: Nominal LHC beam in the SPS (25 ns spacing, 1 batch of 72 bunches)
Cures:
4th harmonic RF system in the bunch-shortening mode with V4 = V1/10
Controlled long. emittance blow-up (by band-limited noise), but then transfer to LHC with limited voltage
Lower transition energy (Q20) – under studies
Q20
2RF
Q26
2RF
Q26
1 RF

## Slide 4: Loss of Landau damping in LHC (longitudinal plane)
Threshold during the 2010 cycle and measurements
Expected loss of Landau damping during the ramp without controlled longitudinal emittance blow-up
Single bunch instability observed during the first ramps and on the flat top in 2010
Un-damped (very slowly damped) injection phase oscillations also observed for multi-bunch 50 ns spaced beam

## Slide 5: Longitudinal instability during LHC ramp
Dipole mode: loss of Landau damping on the flat bottom for emittances below 0.5 eVs (bunch intensity 1.2x1011), instability during ramp with threshold decreasing with energy and longitudinal emittance
Cure: controlled longitudinal emittance blow-up during ramp to ~2eVs
(4σ bunch length of 1.2 ns) also required for IBS and heating problems