## Slide 1: Project X Overview
L. Prost
(for the Project X team)
FNAL
Accelerator Physics forum
CERN
June 17, 2013
Many slides taken from V. Lebedev, S. Nagaitsev, S. Holmes and A. Shemyakin former presentations

## Slide 2: Outline
Project X Facility Goals
Reference Design
Staging Strategy
R&D Program
  Project X Injector Experiment
Our websites:
http://projectx.fnal.gov
http://projectx-docdb.fnal.gov

## Slide 3: What is Project X?
The opportunity to construct and operate the foremost Intensity Frontier facility in the world: multi-MW proton beams available at energies ranging from 1 – 120 GeV
Unique ability to provide high beam power, high duty factor, independent beam formats to multiple experiments simultaneously
Capitalizing on the rapid development of superconducting rf technology
Undertaken by an international collaboration

## Slide 4: The Landscape
M Seidel, PSI
Project-X

## Slide 5: Facility Goals
A neutrino beam for long baseline neutrino oscillation experiments
  2 MW proton source at 60-120 GeV
MW-class low energy proton beams for kaon, muon, neutrino, and nuclei/ nucleon based precision experiments
  Operations simultaneous with the neutrino program
A path toward a muon source for possible future Neutrino Factory and/or a Muon Collider
Possible missions beyond particle physics
  Energy and materials applications

## Slide 6: Project X Schematic
1.0
MW
1 GeV
~5 % duty cycle

## Slide 7: Performance Goals

## Slide 8: Beam(s) Structure
Bunch-by-bunch beam chopping and RF separation after acceleration are two corner stones of the project
  Each experiment can receive its desired bunch structure

## Slide 9: Linac technology map
“Standard” scheme for beam acceleration is used
  Except for acceleration in SRF from low energies
Section | Freq | Energy (MeV) | Cav/mag/CM | Type
RFQ | 162.5 | 0.03-2.1 |  | 
HWR (G=0.1) | 162.5 | 2.1-11 | 8/8/1 | HWR, solenoid
SSR1 (G=0.22) | 325 | 11-38 | 16/8/ 2 | SSR, solenoid
SSR2 (G=0.51) | 325 | 38-177 | 35/21/7 | SSR, solenoid
LB 650 (G=0.61) | 650 | 177-467 | 30/20/5 | 5-cell elliptical, doublet
HB 650 (G=0.9) | 650 | 467-1000 | 42/16/7 | 5-cell elliptical, doublet
HB 650 (G=0.9) | 650 | 1000-3000 | 120/30/15 | 5-cell elliptical, doublet
ILC 1.3 (G=1.0) | 1300 | 3000-8000 | 224 /28 /28 | 9-cell elliptical, quad

## Slide 10: Choice of Main Parameters
Bunch repetition rate of 162.5 MHz is set by RFQ
  Sub-harmonic of the ILC frequency
  The fastest rate compatible with bunch-by-bunch chopping
Beam energies are determined by experimental program
  1 GeV – nuclear physics, nuclear energy and m-to-e
  3 GeV – kaon and muon experiments
Beam current
  5 mA from the ion source
    Bunch-by-bunch chopping allows to create desired bunch patterns and powers for all experiments
  2 mA in 1 GeV linac
    Then the current is equally split between 1 & 3 GeV experiments
  1 mA in 3 GeV linac delivers 3 MW to 3 GeV

## Slide 11: CW Linac – Beam Dynamics
Lattice design & beam dynamics optimization are made utilizing the TRACK, TraceWin and GenLinWin codes.
Rms bunch length
Transverse x- and y– rms envelopes
1 GeV arc is presented as a short drift.

## Slide 12: Emittance growth in CW Linac
Emittance growth is within Project X specifications
en(magenta) and enL (green) rms emittances along the linac Only the 1 GeV part of CW linac is shown Initial longitudinal emittance corresponds to 1.6 keV*nsec

## Slide 13: Particle Loss in SC linac
Intrabeam stripping is the major mechanism resulting in the beam loss
Aperture and Particle density distribution along the linac 100,000 particles tracked in PARTRAN
Beam power losses per unit length

## Slide 14: Staging
Fiscal considerations/constraints have motivated development of a staging plan
Staging principles:
  Compelling physics opportunities at each stage
  Cost of each stage substantially <$1B
  Utilize existing infrastructure to the extent possible at each stage
  Minimize interruptions to the ongoing program at each stage
  Achieve full Reference Design capabilities at end of final stage
Three stage plan developed and presented to DOE/OHEP
Reference Design siting plan developed consistent with staging
Notes: Test
14

## Slide 15: Staging Site Plan

## Slide 16: Linac Beam (Stage 1)
In Stage 1: the Booster injection is 1-ms long (flattop) at 15 Hz
->66.7 ms
Time, ms
0
1
Linac beam
current, mA
To Booster
To 1-GeV program
Pulsed
dipole
OFF
ON

## Slide 17: 1-GeV CW linac in Stage 1
Ion source operates at ~3.6 mA
Chopper removes unwanted bunches to make ave. beam current 1 mA
Bunches are rf-split between the muon and “nuclear” programs

## Slide 18: Linac Beam (Stage 2)
In Stage 2: The 1-GeV linac rf power is upgraded to 2-mA
The Booster injection: ~0.5-ms long (flattop) at 15 Hz
->66.7 ms
Time, ms
0
2
MEBT beam
current, mA
To Booster
To 1-GeV program (1 mA)
and 3-GeV program (1 mA)
Pulsed
dipole
OFF
ON

## Slide 19: Stage-2 CW linac
Ion source at 5 mA
2-mA beam up to 1 GeV
RF bunch splitter at 1 GeV
To 1-GeV Experimental Area
To 1-GeV Arc and 3-GeV linac

## Slide 20: Linac Beam (Stage 3)
In Stage 3: The 3-8 GeV linac is added to inject into the Recycler
The Recycler injection is ~4.4-ms long (flattop) at 10 Hz
->100 ms
Time, ms
0
2
MEBT beam
current, mA
To Pulsed Linac
To 1-GeV program (1 mA)
and 3-GeV program (1 mA)
Pulsed
dipole
OFF
ON

## Slide 21: R&D Program
Goal is to be prepared for a construction start in Q1FY18
  Most likely, Stage 1
Goal of the R&D Program is to mitigate risk: technical/cost/schedule
      The unique capabilities of Project X depend (almost) entirely on the front end, in particular the wideband chopper.
Technical Risks
  Front End
    CW ion source through SSR1
  H- injection system
    Booster in Stage 1, 2; Recycler in Stage 3
  High Intensity Recycler/Main Injector operations
  High Power targets
Cost Risks
  Superconducting rf
    Cavities, cryomodules, rf sources – CW to long-pulse
Project X Injector Experiment (PXIE)

## Slide 22: Front-End R&D Program (as proposed in Oct 2011)
We are building an integrated systems test of the first ~30 MeV of Project X.
  Validate the concept for the Project X front end
  Demonstrate wideband chopper; low-b acceleration
  Operate at full design parameters
Integrated systems test goals:
  1 mA average current with 80% chopping of beam delivered from RFQ
  Efficient acceleration with minimal emittance dilution through ~30 MeV
Beam through b=0.1 , 0.2 CM at ~30 MeV with nearly final parameters (1 mA cw, 5 mA peak, arbitrary bunch chopping)

## Slide 23: PXIE structure
Standard scheme for proton (H-) acceleration
  Ion source and LEBT (30 keV, 5 mA nominal/ 10 mA max DC)
    Beam pre-chopping for machine tuning
  162.5 MHz RFQ (2.1 MeV, 5/10 mA CW)
  MEBT (chopping, 5mA CW->1mA Repetitive Structure )
  2 SC cryomodules accelerating the beam to 20-30 MeV
  HEBT (beam diagnostics)
  50 kW beam dump
Total length ~ 40 m
Collaboration between Fermilab, ANL, LBNL, SNS, SLAC, and Indian institutions

## Slide 24: PXIE Goals
The main specific goals
  Demonstrate the bunch-by-bunch chopping
    Kicker and absorber
  Efficient acceleration of 1mA beam in SRF to at least 15 MeV
    Emittance dilution; halo generation and management
Also, address
  Emittance issues and pre-chopping in LEBT
  Reliable CW RFQ
  MEBT/SRF interface (vacuum, microparticle migration)
  Diagnostics for testing the extinction of the removed bunches to ~10-9
  Gain experience in design and operation of SC cryomodules
    SSR1 cryomodule will be designed and built by Fermilab

## Slide 25: PXIE layout
41 m
PXIE
Cryomodule test stand
Cryoplant
PXIE will be assembled in the existing Cryo Module Test Facility building

## Slide 26: Ion source
H- ion source
  Purchased from D-Pace Inc.
  Was tested and used at LBNL for a year
    Now at Fermilab
30 kV, 15 mA DC, εrms,n_x  0.12µm
Life time 300 hrs
Ground electrode
Port for turbo pump

## Slide 27: LEBT
LEBT
  3 solenoids
  Dipole to accommodate two IS for PX
    Only one at PXIE
  Chopper
    Pre-chopping, MPS, pulse mode
  Possibility of partially un-neutralized transport
  Beam halo scraping
3D model of the first, straight stage of LEBT

## Slide 28: RFQ
Design (LBNL): 4 vanes CW RFQ
  162.5 MHz frequency to make bunch-by-bunch chopping possible
  2.1 MeV energy to exclude residual radiation in the MEBT
Beam current: 1 – 10 mA; εn,rms < 0.25 µm ε||n,rms ≤1.0 keV-ns Length: ~4.4 m
  Simulations completed
    RF, beam, thermal, stress
  Finalizing the production drawings
  Manufacturing tests
RF coupler has been designed

## Slide 29: MEBT
Transverse focusing – 9 quadrupole doublets/triplets
  Small β-function variation
  Quads/dipole correctors are being designed by BARC, India
Longitudinal focusing – 3 bunching cavities
  Production drawings preparation
MEBT sections and optics. 3σ envelopes of passing bunches – thin lines, removed bunches- thick lines.
Red squares- quads, blue – bunching cavities.
Frequency 162.5 MHz
Max voltage 100 kV
Gap 2x23 mm
Max power loss 1.5 kW
Design: I. Terechkine et al.

## Slide 30: Chopping system
Undesired bunches are removed by the MEBT chopper
  Two kickers separated by 180º and working in sync (next slide)
  Removed and passing bunches are separated at the absorber by 6σy
  Large gas load from absorber, ~1 mTorr·l/s
    2500 l/s turbo pumping at the absorber and differential pumping
Developed a concept of a 21 kW absorber (x2 full nominal power)
  29 mrad incident angle
  Mo alloy TZM
  Testing ¼ size prototype with e-beam
Two kickers separated by 180º
Absorber
Differential pumping

## Slide 31: Kicker
Travelling – wave, broadband kickers: 50 and 200 Ohm versions
  0.5m, ±250V on each plate, 16mm gap; 6σ beam length is 1.3 ns
50 Ohm
  25 electrodes per plate connected in vacuum by cables
    Finalizing the production drawings
  Commercial linear amplifier and pre-distortion
    Lower power driver successfully tested
200 Ohm
  Helix as travelling-wave structure
    RF simulations, modeling, concept development
3D model A.Chen, D.Sun
RF model G. Saewert
  Driver: broadband, DC coupled switches in push-pull configuration
    Fermilab development
    Single switch: tested to 0-500V
    Complete driver: tested to 0-100 V

## Slide 32: SRF cryomodules
Two cryomodules operating at 2K, HWR and SSR1
  Half Wave Resonators (HWR) and Single Spoke Resonators (SSR1)
  Warm gap between cryomodules; fast vacuum valves on both sides
In both cryomodules
  Solenoidal focusing
    No magnetic steel; backing coil to reduce fringe field
  BPM and dipole correctors in each solenoid
Structure of HWR cryomodule
  8 cavities, 8 solenoids arranged as 8x ( S C )
  Starts with a solenoid to mitigate H2 influx from MEBT
Structure of SSR1 cryomodule
  8 cavities, 4 solenoids arranged as 4x ( C S C )
  Separated coils of dipole correctors allow creating of skew-quads
  The first upstream element is a cavity to improve longitudinal dynamics
Warm transition box between CMs

## Slide 33: HWR
  Cavity and cryomodule design is complete
  Prototypes of 10-kW RF coupler and SC solenoid with steering coils have been built and successfully tested
  BPM prototype has been built and will be tested with beam in FY13
  Nb parts for all cavities will be fabricated in FY13
  Two prototype SC cavities will be tested in FY14
Beam energy: 2.1-11MeV
Frequency 162.5 MHz
CM length (flange-to-flange): 5.9 m
βg 0.11
Cavity voltage 1.7 MV
Design and production by Argonne National Lab
Solenoid installed in He vessel
Cavity with coupler
BPM parts
Cavity parts

## Slide 34: SSR1
  Design of major components is complete
    Cavity, tuner, coupler, solenoid, current leads, helium vessel, support
  Design of cryomodule to be complete in Fall 2013
  First production batch of 10 cavities is complete
    Tests proceed well
    Prototypes of coupler, solenoid, and helium vessel are close to production
Beam energy: 11-25 MeV
Frequency 325 MHz
CM length (flange-to-flange): 5.4 m
βg 0.22
Cavity voltage 2 MV
3D model of cavity with tuners

## Slide 35: HEBT
D. Johnson
Functions:
  Primary 50 kW beam dump
  Instrumentation to characterize beam parameters and measure efficiency of MEBT bunch-by-bunch chopper
Status:
  Preliminary design of optics, absorber, and shielding complete
  deflecting cavity is being designed
  Instrumentation specifications in progress

## Slide 36: Plans
FY2013 – beam from ion source (at Fermilab)
FY2015 – beam from RFQ
FY2017 – Stage 1
  Ion source, LEBT, RFQ at full power
  Full MEBT with prototype kickers, prototype absorber, temporary dump, bunchers, some diagnostics
  Cryo system
  SSR1 CM – cold and RF powered, no beam
Aug 2017- Stage 2
  HWR CM – cold and RF powered, no beam
Aug 2018- Stage 3
  HEBT, final MEBT kickers, final 50 kW beam dump, 1-mA beam with required structure delivered to the dump

## Slide 37: Backup Slides

## Slide 38: Reference Design
A complete design concept exists (Reference Design Report)
3 GeV CW superconducting H- linac with 1 mA average beam current.
  Enhanced performance of the existing proton complex
  Spallation-based program (nucleon/energy applications) at 1 GeV (1 MW)
  Rare processes programs at 3 GeV (3 MW)
  Flexible provision for variable beam structures to multiple users
3-8 GeV pulsed linac capable of delivering 340 kW at 8 GeV
  Enhanced performance for short and long-baseline neutrino programs
  Establishes a path toward a muon-based facility
Upgrades to the Recycler and Main Injector to provide ≥ 2 MW to the neutrino production target at 60-120 GeV.
Utilization of a CW linac creates a facility that is unique in the world, with performance that cannot be matched in a circular accelerator based facility.
Notes: ADS Development with Nuclear Energy Applications

## Slide 39: Reference Design Performance Goals
Linac
Particle Type H-
Beam Kinetic Energy 3.0 GeV
Average Beam Current 1 mA
Linac pulse rate CW
Beam Power to 1 GeV program 1000 kW
Beam Power to 3 GeV program 2870 kW
Pulsed Linac
Particle Type H-
Beam Kinetic Energy 8.0 GeV
Pulse rate 10 Hz
Pulse Width 4.3 msec
Cycles to Recycler/MI 6
Particles per cycle to Recycler/MI 2.71013
Beam Power 340 kW
Beam Power to 8 GeV program 170 kW
Main Injector/Recycler
Beam Kinetic Energy (maximum) 120 GeV
Cycle time 1.2 sec
Particles per cycle 1.51014
Beam Power at 120 GeV 2400 kW
simultaneous

## Slide 40: Choice of Main Parameters
Bunch repletion rate of 162.5 MHz is set by RFQ
  Sub-harmonic of the ILC frequency
  The fastest rate compatible with bunch-by-bunch chopping
Beam current
  0-10 mA from the ion source
    Bunch-by-bunch chopping allows to create desired bunch patterns and beam powers for all experiments
  2 mA up to 1 GeV
    Then the current is equally split between 1 & 3 GeV experiments
  1 mA in 1 to 3 GeV linac (delivers 3 MW to 3 GeV)

## Slide 41: Project X and PXIE
Project X is an Intensity Frontier accelerator providing MW-scale proton beam to many users quasi- simultaneously
  Acceleration in SRF from low energies
  Constant power in time scale >µs; adjustable structure of the bunch train
  Accomplished by bunch-by-bunch chopping in MEBT and RF separation after acceleration to the required energy
Addressed by the Project X Injector Experiment, PXIE