## Slide 1: Benchmarking CST impedance simulations and application to the BGV project
August 21st 2013
BE-ABP
Bérengère Lüthi – Summer Student 2013
Supervisors : Benoît Salvant and Carlo Zannini
Many thanks to Serena Persichelli, Elias Metral, Massimiliano Ferro-Luzzi, Plamen Hopchev, Ray Veness, Alexej Grudiev, Elena Shaposhnikova.

## Slide 2: Context
CST is used a lot at CERN
Can we trust the code ?
Just the start of a long process to understand the tools ans their limits
Two solvers :
Eigenmode solver : no beam, calculates the eigenmodes of the cavity (frequency domain method), can use tetrahedral or cartesian mesh, no open boudaries conditions
Wakefield solver : with a beam, calculates the wakepotential (time domain method),only cartesian mesh, open boundaries conditions possible

## Slide 3: Agenda
Longitudinal Impedance Benchmarks
Transverse Impedance Benchmarks
Application to BGV studies

## Slide 4: Longitudinal Impedance
Plan of studies
Simple cavity
Comparison betwen two solvers : Eigenmode and Wakefield.
      Changing length and radius of the cavity
      Changing conductivity
      Studies on both magnitude and Q
      First mode only
      First check with ferrite materials

## Slide 5: Longitudinal Impedance
Two conventions (from Serena)
ELECTRIC/CIRCUIT convention
Z=
Units : Ohm (or CircuitOhm)
Wakefield solver ?
LINAC convention
Units : LinacOhm
Eigenmode Solver


Calculations from simulation results with the Eigenmode solver

## Slide 6: Longitudinal Impedance
Strategy suggested
Wakefield values should be used as references when the unit Omh is used.
With the Eigenmode solver it is better to talk about LinacOhm or adapt the value to obtain Ohm.
Already mentionned for instance in two studies:
Calculation of Wakefields and Higher Order Modes for the New Design of the Vacuum Chamber of the CMS Experiment for the HL-LHC
by R. Wanzenberg and O. Zagorodnova
Simulation of Longitudinal and Transverse Impedances of Trapped Modes in LHC Secondary Collimator
by A. Grudiev

## Slide 7: Longitudinal Impedance
Cavity used
Conductivity = 1e3 S/m
(in order to get reasonnable
simulation time)
Lossy Metal with both solvers
Double parameter sweep :
Radius from 30 to 60 cm
Length from 20 to 60 cm
radius
length

## Slide 8: Longitudinal Impedance
Example : length = 30cm
and radius = 40cm
Wakefield solver
Mesures with a fit :
Z =
HWHM
Rs
Wakelength (in cm)
Wakepotential
Frequency in Ghz
Impedance in Ohm
Notes: Half width half maximum

## Slide 9: Longitudinal Impedance
Results : magnitude
Chart: Rs Ratio VS wakelength
| 12000 | 20000 | 50000
 | 2.2898 | 2.2432 | 2.2331
 | 2.3466 | 2.226 | 2.2457
 | 2.4041 | 2.2125 | 2.1819
 | 2.45 | 2.2178 | 2.1798
 | 2.4986 | 2.2418 | 2.1577
 | 2.366 | 2.2656 | 2.2312
 | 2.5455 | 2.324 | 2.252
 | 2.7022 | 2.4522 | 2.2885
 | 2.8486 | 2.4885 | 2.342
 | 2.9346 | 2.4955 | 2.3347
 | 2.3678 | 2.1721 | 2.107
 | 2.6243 | 2.2553 | 2.12
It seems to be converging to a ratio close to 2
~10% error even though the wake decayed by factor 100
One point : ratio of the shunt impedance with Eigenmode with a particular geometry to the shunt impedance with wakefield with the same geometry
Example (wakefield) : length = 30cm and radius = 40cm
Wakelength in cm
Frequency in Ghz
Z in Ohm
Notes: 12 000 : ~5
20 000 : ~10
50 000 : ~100

## Slide 10: Longitudinal Impedance
Results : Q factor (perturbation)
10% to 20% error
Chart: Q Ratio VS Wakelength
| 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000 | 50000
 | 1.1689 | 1.1414 | 1.1261 | 1.1193 | 1.1077 | 1.1449 | 1.1648 | 1.1594 | 1.2788 | 1.2812 | 1.0725 | 1.071 | 1.0737 | 1.0738 | 1.0717 | 1.1864 | 1.2353 | 1.1188 | 1.0753 | 1.0642
Mesures with a fit :
Z =
Frequency in Ghz
Impedance in Ohm
Longitudinal impedance with CST PS
HWHM
Rs

## Slide 11: Longitudinal Impedance
What if we change the conductivity from S/m to S/m ?
Note : issue when changing
the conductivity in Eigenmode
CST support contacted
No parameter sweep possible
 Ratio more ~2.5
Longitudinal impedance after a post processing on CST PS
Longitudinal impedance with CST PS
Longitudinal wake potential with CST PS
Notes: Walength ~20

## Slide 12: First checks with ferrite materials
Wakefield simulations for a
ferrite loaded cavity:
Longitudinal wake potential from CST PS with increasing number of mesh cells from 256k to 2M
 Computed parameters
Q=fres/(2*HWHM)=4.34
fres=570 MHz
R=303 Ohm
R/Q=70 Ohm
 Seems to have converged with number of mesh cells
Longitudinal impedance from CST PS with increasing number of mesh cells from 256k to 2M
Ferrite
material

## Slide 13: First checks with ferrite materials
Eigenmode simulations for the same ferrite loaded cavity:
Note: many problems, even after the new release and the hotfix (following the email of Serena)
Note: perturbation values (shunt impedance and Q factors) should be used with lossy materials
 Computed parameters from wakefield (CST PS)
Q=fres/(2*HWHM)=4.34
fres=572 MHz
R=303 Ohm
R/Q=70 Ohm
 Seems to have converged with number of mesh cells
Computed parameters from eigenmode (CST EM):
1st mode
Q(lossy eigenmode)=3.05
fres=566 MHz
R(from lossy eigenmode)=346 LinacOhm
R/Q= 114 LinacOhm
 Eigenmode solver converged
Orders of magnitude between the two solvers are the same, but significant difference in the Q (50%)
R/Q looks reasonable
But which code should we believe?
We should also check with HFSS.
Ferrite
material

## Slide 14: Agenda
Longitudinal Impedance Benchmarks
Transverse Impedance Benchmarks
Application to BGV studies

## Slide 15: Transverse Impedance
Plan of studies
Simple cavity
Comparison between two solvers : Eigenmode and Wakefield
      Studies on both magnitude and Q
      First mode only

## Slide 16: Transverse Impedance
Wakefield Solver
Direct values in results
Eigenmode Solver
Uses longitudinal values and Panofski-Wenzel equation to calculate transverse impedance
Z=
 Conclusion : need a way to know which modes really are transverse modes
Simulation and calculation of the transverse modes.
Radius = 50 mm and length = 20 mm
radius
length

## Slide 17: Transverse Impedance
Idea to make the distinction between real and fake mode with the Eigenmode solver :
If not real transverse mode : noise
= f(d²) if real mode

## Slide 18: Transverse Impedance
Cavity used
Conductivity = 1e3 S/m
(in order to get reasonnable
simulation time)
Lossy Metal with both
Solvers
Double parameter sweep :
Radius from 40 to 60 mm
Length from 30 to 60 mm
radius
length

## Slide 19: Transverse Impedance
Results : magnitude
 ~10% error
Chart: Rs Ratio VS Wakelength
| 14000 | 14000 | 14000 | 14000 | 14000 | 14000 | 14000 | 14000 | 14000 | 14000 | 14000 | 14000 | 14000 | 14000
 | 2.2222 | 2.2222 | 2.1 | 2.2761 | 2.2751 | 2.7086 | 2.2753 | 2.3083 | 2.2928 | 2.2888 | 2.2574 | 2.2706
Rs
Wakepotential with CST PS
Transverse Impedance (x direction) with CST PS
Z in Ohm/5mm

## Slide 20: Transverse Impedance
Results : Q factor
 ~20% error  no fit
Chart: Q Ratio VS Wakelength
| 14000 | 14000 | 14000 | 14000 | 14000 | 14000 | 14000 | 14000 | 14000 | 14000 | 14000 | 14000 | 14000 | 14000
 | 1.1832 | 1.1706 | 1.5276 | 1.186 | 1.1659 | 1.438 | 1.2435 | 1.1987 | 1.2356 | 1.1939 | 1.2777 | 1.1959
Wakepotential with CST PS
Transverse Impedance (x direction) with CST PS

## Slide 21: Longitudinal and Transverse Impedance
Conclusions
In general it seems like we can trust the code but
Eigenmode solver is certainly preferable when using high conductivity
One should be careful when using ferrite materials : not sure yet which one to believe
One should be careful to the convention used (Ohm VS LinacOhm)
Wakefield solver uses the circuit convention
Safer to fit a parabola to identify transverse modes

## Slide 22: Agenda
Longitudinal Impedance Benchmarks
Transverse Impedance Benchmarks
Application to BGV studies

## Slide 23: BGV Studies
What is a BGV ?
BGV stands for Beam Gas Vertexing
studies for a beam shape imaging detector, based on vertex reconstruction of beam-gas interactions.
The goal is also to provide transverse emittance measurements at the LHC.

## Slide 24: BGV Studies
What is a BGV ?
Structure

## Slide 25: BGV Studies
Plan of study
Radius of 147mm
Radius of 106mm
    Influence of the length
    Influence of the taper
    Influence of the angle of the taper

## Slide 26: BGV Studies
147mm radius
 Tapers don’t kill all the modes
 Many longitudinal resonances whatever the angle from 800 MHz onwards.
Angle 1=10 degrees
Scan over Angle 2
Eigenmode simulations
Frequency in GHz
Longitudinal impedance in LinacOhm

## Slide 27: BGV Studies
Not monotonic
The length of the cavity should not be too small
Frequency of the modes is not plotted, but is also important to assess their effects
106 mm radius (smaller radius push frequencies higher : > 1Ghz)
Copper coating (increases shunt impedance by a factor ~ 6,7 for 316LN)
Rs in LinacOhm

## Slide 28: BGV Studies
 The longer taper, the better
Influence of the taper – L = 0.5m
L
l
l
Rs in LinacOhm

## Slide 29: BGV Studies
 The longer taper, the better
Influence of the taper – L = 1m
L
l
l
Rs in LinacOhm

## Slide 30: BGV Studies
 The longer taper, the better
Influence of the taper – L = 1.5m
L
l
l
Rs in LinacOhm

## Slide 31: BGV Studies
106 mm radius (smaller radius push frequencies higher)
Copper coating (increases shunt impedance by a factor ~ 6,7 for 316LN)
Full length of about 2 m (taper included)
Cavity length increases
 Taper length decreases
L
l
l
L+2l = 2 m

## Slide 32: BGV Studies
The longer the taper, the better (for the symmetric case)
Even with copper coating, well below the limit below 1.5 m of flat length
Rs in LinacOhm
Zoom below the limit
L
l
l
L+2l = 2 m

## Slide 33: BGV Studies
Total length: 2 m
More realistic : Copper and Steel structure
Longitudinal studies
Angle 2=5 degrees
Scan over Angle 1
The lower the tapering angle, the better
Under the limit even with angle close to 90°
Copper
Stainless Steel 316LN
Copper
Rs in LinacOhm

## Slide 34: BGV Studies
Total length: 2 m
Transverse studies
Angle 2=5 degrees
Scan over Angle 1
Copper
Stainless Steel 316LN
Copper
Seems ok but still need some precision
Waiting fot the final structure to do more accurate simulations
Transverse Impedance in LinacOhm/m

## Slide 35: BGV Project
Conclusions
106 mm radius helped a lot
With the Steel/Copper structure, longitudinal and transverse modes seem to be under the acceptable limit
We are still waiting for the final structure to confirm these first studies

## Slide 39
radius
length

## Slide 40: Transverse Impedance
Cavity used
Conductivity = 1e3 S/m
Double parameter sweep :
Radius from 30 to 60 mm
Length from 20 to 60 mm
radius
length

## Slide 41: A more realistic geometry
106 mm radius (smaller radius push frequencies higher)
Copper coating (increases shunt impedance by a factor ~ 6 for 316LN)
Full length of about 2 m (taper included)
Cavity length increases
 Taper length decreases
L
l
l
L+2l = 2 m

## Slide 42: Zoom below the limit
The longer the taper, the better (for the symmetric case)
Even with copper coating, well below the limit below 1.5 m of flat length (with Ploss of 40 W  is it acceptable from mechanical point of view?).

## Slide 43: Longitudinal impedance at high frequency
Total length: 2 m
Copper and Steel structure
Angle 2=5 degrees
Scan over Angle 1
The lower the tapering angle, the better
Under the limit even with angle close to 90°
Copper
Stainless Steel 316LN
Copper

## Slide 44: Longitudinal impedance at high frequency
Total length: 2 m
Angle 2=5 degrees
Scan over Angle 1
Copper
Stainless Steel 316LN
Copper

## Slide 45: Transverse impedance at high frequency
Total length: 2 m
Angle 2=5 degrees
Scan over Angle 1
Copper
Stainless Steel 316LN
Copper