## Slide 1: Tools and instruments used for beam impedance measurements
O.Berrig & J.Kuczerowski

## Slide 2
When measuring on equipment that changes length or equipment with horizontal or vertical offset;
we use a measuring bench
This bench is in building 113. It belongs to V.Baglin and A.Vidal. They kindly allow us to use it.

## Slide 3
When measuring on equipment with several inputs/outputs, we need to borrow a 4 port network analyzer (e.g. F.Caspers, M.Ehret/M.Wendt, M.Barnes )
Please Note also, that we need connectors, which converts from N-Type to SMA
A 4 port network analyzer needs an automatic calibration unit, otherwise the calibration will take too long time (16 combinations for the channels)

## Slide 4
We need to buy SUCO boxes and in general we need a budget for the mechanical workshop: Flanges, etc.
Flange with moving SUCO box. Used for measuring transverse impedance
Screws made of plastic (non conducting)

## Slide 5
Tools, matching resistors (carbon), wires, coax cables (good ones), hybrids for transverse beam impedance measurements, Network Analyzer, etc.
Hybrid
Clamp
Soldering iron
The laser is used to measure the length of the equipment, so that the wire can be cut in the right length
Probe for precise measure of the Q-value
Attenuator

## Slide 6
Foreseen purchases for 2014
De-block of present commands: ~ 1000 CHF
Hybrid: ~ 3000 CHF
(We really need to buy two hybrids
– one at each end of the DUT –
but it was agreed with Oliver that
we buy one in 2014 and another in 2015)
Cables: ~ 2000 CHF
Mechanical workshop: ~ 5000 CHF (flanges)